## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 6 The Link Layer
and LANs
Acknowledgement: Based on the textbook’s website: https://gaia.cs.umass.edu/kurose_ross/index.php
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
lighter header font
Updated datacenter slides, day-in-the-life
8.2 (July 2023): changes from 8.0
Minor updates throughout, including removal of master/slave
A few new slides added (transportation analogy, UMass LAN example, extended LANs)
Couple of not-used slides now hidden.

## Slide 2: Link layer and LANs: our goals
understand principles behind link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
  local area networks: Ethernet, VLANs
datacenter networks
instantiation, implementation of various link layer technologies

## Slide 3: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 4: Link layer: introduction
terminology:
hosts, routers: nodes
communication channels that connect adjacent nodes along communication path: links
  wired , wireless
  LANs
layer-2 packet: frame, encapsulates datagram
mobile network
enterprise
network
national or global ISP
datacenter
network
link layer has responsibility of
transferring datagram from one node
to physically adjacent node over a link

## Slide 5: Link layer: context
datagram transferred by different link protocols over different links:
  e.g., WiFi on first link, Ethernet on next link
each link protocol provides different services
  e.g., may or may not provide reliable data transfer over link

## Slide 6: Transportation analogy
transportation analogy:
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
transportation mode = link-layer protocol
travel agent = routing algorithm
Princeton
JFK
Geneva
Lausanne

## Slide 7: Link layer: services
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses in frame headers identify source, destination (different from IP address!)
reliable delivery between adjacent nodes
  we already know how to do this!
  seldom used on low bit-error links
  wireless links: high error rates
    Q: why both link-level and end-end reliability?
…
…
Cable access
cellular
WiFi
Ethernet LANs
Notes: reliable delivery between adjacent nodes
Not always
Rdt likes we studied in transport layer
Reliable is not as important is correctness. How is correctness assured?
Wireless is subjected to noise, interference and has high bit error rate.
Why

## Slide 8: Link layer: services (more)
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects errors, signals retransmission, or drops frame
error correction:
  receiver identifies and corrects bit error(s) without retransmission
half-duplex and full-duplex:
  with half duplex, nodes at both ends of link can transmit, but not at same time
…
…
Cable access
cellular
WiFi
Ethernet LANs
Notes: Error detection in the link layer is usually more sophisticated and is implemented in hardware. Error correction is similar to error detection, except that a receiver not only detects when bit errors have occurred in the frame but also deter- mines exactly where in the frame the errors have occurred (and then corrects these errors).

## Slide 9: Host link-layer implementation
in each-and-every host
link layer implemented on-chip or in network interface card (NIC)
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
cpu
memory
host bus
(e.g., PCI)
network interface
application
transport
network
link
link
physical
Notes: The Ethernet capabilities are either integrated into the motherboard chipset or implemented via a low-cost dedicated Ethernet chip. For the most part, the link layer is implemented on a chip called the network adapter, also sometimes known as a network interface controller (NIC). The network adapter implements many link layer services including framing, link access, error detection, and so on. Thus, much of a link-layer controller’s functionality is implemented in hardware. For example, Intel’s 700 series adapters [Intel 2020] implements the Ethernet protocols we’ll study in Section 6.5; the Atheros AR5006 [Atheros 2020] controller implements the 802.11 WiFi protocols we’ll study in Chapter 7.
Figure 6.2 shows that while most of the link layer is implemented in hardware, part of the link layer is implemented in software that runs on the host’s CPU. The software components of the link layer implement higher-level link-layer functionality such as assembling link-layer addressing information and activating the controller hardware. On the receiving side, link-layer software responds to con- troller interrupts (for example, due to the receipt of one or more frames), handling error conditions and passing a datagram up to the network layer. Thus, the link layer is a combination of hardware and software

## Slide 10: Interfaces communicating
controller
physical
memory
CPU
controller
physical
cpu
memory
application
transport
network
link
link
physical
application
transport
network
link
link
physical
sending side:
encapsulates datagram in frame
adds error checking bits, reliable data transfer, flow control, etc.
receiving side:
looks for errors, reliable data transfer, flow control, etc.
extracts datagram, passes to upper layer at receiving side
linkh
linkh
datagram
datagram
datagram

## Slide 11: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 12: Error detection
EDC: error detection and correction bits (e.g., redundancy)
D: data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
datagram
D
EDC
d data bits
bit-error prone link
D’
EDC’
all
bits in D’
OK
?
N
detected
error
otherwise
datagram

## Slide 13: Parity checking: one-dimensional
single parity bit for d data bits:
We consider even parity in this lecture
  Even parity: set parity bit to 0 (1) if there is an even (odd) number of 1’s
  Odd parity: set parity bit to 0 (1) if there is an odd (even) number of 1’s
0111000110101011
1
parity bit
d data bits
At receiver:
compute parity of d received bits
compare with received parity bit – if different than error detected
Can detect odd number of bit errors (1,3…) but not even number of bit errors (2,4…), which do not affect parity bit
  e.g., error of 1 bit causes the parity bit to flip, but error of 2 bits does not
  The vast majority of errors are single bit flips
IMPORTANT

## Slide 14: Parity checking: two-dimensional
multiple parity bits for a two-dimensional array of data bits:
Transmit data as a block of i rows of j bits per row and add parity bit to each row and each column.
  For i rows and j columns, compute j column parity bits (last row), i row bits (last column), and one corner parity bit as the sum of row and column parities.
  All rows are concatenated and sent out. For the example, sent:
  1 0 1 0 1 1 1 1 1 1 0 0 0 1 1 1 0 1 0 0 1 0 1 0
Can detect and correct single-bit errors (without retransmission at the TCP layer)
  But may (or may not) detect, and cannot correct, multiple bit errors
d1,1
d2,1
di,1
. . .
d1,j+1
d2,j+1
di,j+1
. . .
. . .
d1,j
d2,j
di,j
. . .
di+1,1
di+1,j+1
di+1,j
. . .
. . .
. . .
. . .
row parity
column
parity
0 0 1 0 1
0 1 1 1 0
1 0 1 0 1
1 1 1 1 0
1
0
1
0
no errors:
parity
error
parity
error
0 1 1 1 0 1
1 0 1 0 1 1
1 0 1 1 0 1
0 1 1 0 1 0
detected
and
correctable
single-bit
error:
At receiver:
compute the row, column and corner parity bits, and compare with received parity bits
  If sum of # row parity errors and # column parity errors is odd, then the corner parity bit also has an error; if even, then the corner parity bit has no error
For the example, receiver detects 2 parity errors, hence the erroneous data bit can be identified by the row and column numbers of the parity errors:
Received: 1 0 1 0 1 1 1 0 1 1 0 0 0 1 1 1 0 1 0 0 1 0 1 0
Computed: 1 0 1 0 1 1 1 0 1 1 0 1 0 1 1 1 0 1 0 1 1 0 1 0
IMPORTANT
Notes: All rows are concatenated and sent out, e.g., 1 0 1 0 1 1 1 1 1 1 0 0 0 1 1 1 0 1 0 0 1 0 1 0
two-dimensional parity: detect and correct single bit errors
We consider even parity in this lectyure
  Even parity: set parity bit to 0 (1) if there is an even (odd) number of 1’s
  Odd parity: set parity bit to 0 (1) if there is an odd (even) number of 1’s

## Slide 15: Quiz: Number of Parity Errors
0 0 1 0 1
0 1 1 1 0
1 0 1 0 1
1 1 1 1 0
1
0
1
0
no errors:
parity
error
parity
error
0 1 1 1 0 1
1 0 1 0 1 1
1 0 1 1 0 1
0 1 1 0 1 0
1-bit error causes 1 row parity error, 1 column parity error
parity
error
0 1 1 1 0 1
1 0 1 0 1 1
1 0 1 1 1 0
0 1 1 0 0 0
parity
error
2-bit error causes 2 row parity errors
parity
error
0 1 1 1 1 0
1 0 1 0 0 0
1 0 1 1 0 0
0 1 1 0 1 1
3-bit error causes 1 row parity error, 2 column parity error, and 1 corner parity error
parity
error
parity
error
0 0 1 1 1 1
1 1 1 0 0 1
1 1 1 1 0 0
0 0 1 0 1 0
4-bit error causes NO parity error, hence cannot be detected
0 0 1 0 1
0 1 1 1 0
1 0 1 0 1
1 1 1 1 0
1
0
1
0
2-bit error causes
_2_row parity errors
_2_column parity errors
_0_corner parity errors
0 0 1 0 1
0 1 1 1 0
1 0 1 0 1
1 1 1 1 0
1
0
1
0
0 0 1 0 1
0 1 1 1 0
1 0 1 0 1
1 1 1 1 0
1
0
1
0
IMPORTANT
2-bit error causes
_3_row parity errors
_3_column parity errors
_0_corner parity errors
2-bit error causes
_2_row parity errors
_4_column parity errors
_0_corner parity errors
Notes: 4
7
6

## Slide 16: Internet checksum (review, see section 3.3)
sender:
treat contents of UDP segment (including UDP header fields and IP addresses) as sequence of N-bit integers, where N may be 4, 8, 16…
checksum: addition (one’s complement sum) of the sequence of integers
  One’s complement sum is defined as sum modulo 2N, and adding any overflow of high order bits back into low-order bits, then taking one’s complement (invert all bits)
checksum value put into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  not equal - error detected
  equal - no error detected. (But maybe errors nonetheless)
Goal: detect errors (i.e., flipped bits) in transmitted segment
IMPORTANT
Notes: Will this scheme detect all single errors? Double errors? Triple errors? Show that this scheme cannot detect some four-bit errors.
A single error will cause both the horizontal and vertical parity checks to be wrong.
Two errors will also be easily detected. If they are in different rows, the row parity will catch them. If they are in the same row, the column parity will catch them.
Three errors will also be detected. If they are in the same row or column, that row’s or column’s parity will catch them. If two errors are in the same row, the column
parity of at least one of them will catch the error. If two errors are in the same
column, the row parity of at least one of them will catch the error. If they are at
different row, the row parity of each of them will detect the error. A 4-bit error in
which the four error bits lie on the four corners of a rectangle cannot be caught
since there are two errors in each row and column.
To obtain the checksum, we need to calculate the ones complement of the ones complement sum of the words. The ones complement sum is same as sum modulo 24 and adding any overflow of high order bits back into low-order bits:
00111010 = 1101
110111001001+1 = 1010
1010+10010011+1=0100.
So, the Internet checksum is the ones complemnet of 0100, or 1011.

## Slide 17: Internet checksum: an example
One’s complement sum for 16-bit integers is defined as sum modulo 2N, N=16, and adding any overflow of high order bits back into low-order bits, then taking one’s complement
sum
checksum
Note: when adding numbers, a carryout from the most significant bit needs to be added to the result
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
IMPORTANT

## Slide 18: Internet checksum: weak protection!
example: add two 16-bit integers
sum
checksum
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
0 1
1 0
Even though numbers have changed (bit flips), no change in checksum!
IMPORTANT

## Slide 19: Example in Decimal Number
Make a number divisible by 9
Example: 823 is to be sent
Left-shift: 8230
Divide by 9, find remainder: 4
Subtract remainder from 9: 9-4=5
Add the result of step 3 to step 1: 8235
Check that the received result is divisible by 9. If not, then has error
Detects all single-digit errors: 7235, 8335, 8255, 8237
Detects several multiple-digit errors: 8765, 7346, 7335, 8775, ...
Does not detect transpositions: 2835

## Slide 20: Cyclic Redundancy Check (CRC)
more powerful error-detection coding
D: data bits (given, think of these as a binary number)
G: bit pattern (generator), of r+1 bits (given, specified in CRC standard)
sender: compute r CRC bits, R, such that <D,R> exactly divisible by G (mod 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
  widely used in practice (Ethernet, 802.11 WiFi)
<D,R> = D 2r XOR R
*
formula for these bits
r CRC bits
d data bits
D
R
bits to send

## Slide 21: Exclusive OR (XOR) for Modulo 2 Arithmetic
0 XOR 0 = 0 (Same Bits)
1 XOR 1 = 0 (Same Bits)
1 XOR 0 = 1 (Different Bits)
0 XOR 1 = 1 (Different Bits)
With XOR arithmetic, addition + and subtraction - operations are the same
  1111 + 1010
  = 1111 - 1010
  = 1111 XOR 1010
  = 0101

## Slide 22: Modulo 2 Addition, Multiplication
Addition:
1 | 0 | 0
+1 | +0 | +1
0 | 0 | 1
1-bit
2-bit
1 | 00 | 01 | 10 | 11 | 110
+0 | +11 | +11 | +11 | +11 | +101
1 | 11 | 10 | 01 | 00 | 011
3-bit
1 0 0
×1 ×0 ×1
1 0 0
Multiplication:
1-bit
2-bit
1 | 00 | 01 | 10 | 11
×0 | ×11 | ×11 | ×11 | ×11
0 | 00 | 01 | 10 | 11
 | 0 0 | 0 1 | 1 0 | 11
 | 000 | 011 | 110 | 101

## Slide 23: Modulo 2 Division
001
0 0
01
10 11011
1 0
010
10
001
0 0
011
10
01
116 110 13 1514 10 1101
13 10
21 010
1 3 1 0
84
7 8
6
Decimal Arithmetic:
1514/13=116, w/ remainder 6
1101
Mod-2 Arithmetic:
1101/10=110, w/ remainder 01
11011/10=1101, w/ remainder 01

## Slide 24: Cyclic Redundancy Check (CRC): Example 1
Sender wants to compute R such that for some integer n:
  D . 2r XOR R = nG
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
D.2r
G
R = remainder [ ]
... or equivalently (XOR R both sides):
  D . 2r = nG XOR R
... which says:
if we divide D . 2r by G, we want remainder R to satisfy:
1 0 0 1
1 0 1 0
1 0 1
0 0 0
1 0 0 1
1 0 0 1
1 0 0 1
0 0 0
1 1 0
1 1 0 0
1 0 1 0
0 1 1
0 1 1
D
R
1 0 0 1
G
0 0 0
1 0 1 1 1 0
2r (here, r=3)
*
1
0
1
algorithm for
computing R
Example: D=101110, G=1001, r=3
  D . 2r = 101110000, R=011

## Slide 25: Cyclic Redundancy Check (CRC): Example 1
D . 2r + R = D . 2r XOR R
= 101110000 XOR 011
= 101110011
It must be divisible by G=1001, i.e. remainder of the division is 0,
D . 2r R is divisible by G, or
D . 2r XOR R = nG
1 0 0 1
1 0 1 0
1 0 1
0 0 0
1 0 0 1
1 0 0 1
1 0 0 1
0 0 0
1 1 0
1 1 0 1
1 0 0 1
0 0 0
0 1 1
D
R
1 0 0 1
G
0 1 1
1 0 1 1 1 0
2r+R (here, r=3)
*
1
0
1

## Slide 26: Cyclic Redundancy Check (CRC): Example 2
Example 2: D=1011010010, G=110010, r=5
  D . 2r = 101101001000000, R=01000
1 1 0 0 1 0
1 1 1 1 1 0
1 1 0 0 1 0
G
1 1 0 0 1 0
0 0 1 0 0 0 0 0 0
1 0 1 1 0 1
1 1 0 0 0 1
1 1 0 0 1 0
1 1 0 0 0 0
1 1 0 0 1 0
0 1 0 0 0
1 1 0 1 0 0 0 1 0 0
R
Error Detection and Correction 2: Cyclic Redundancy Check
https://www.youtube.com/watch?v=6gbkoFciryA

## Slide 27: Cyclic Redundancy Check (CRC): Example 3
1 1 0 0 1 0
1 1 1 1 1 0
1 1 0 0 1 0
1 1 0 0 1 0
0 0 1 0 0 1 0 0 0
1 0 1 1 0 1
1 1 0 0 0 1
1 1 0 0 1 0
1 1 0 0 1 0
1 1 0 0 1 0
0 0 0 0 0
1 1 0 1 0 0 0 1 0 0
R
G
D . 2r + R = D . 2r XOR R
= 101101001000000 XOR 01000
= 101101001001000
It must be divisible by G= 110010, i.e. remainder of the division is 0,
D . 2r XOR R is divisible by G, or
D . 2r XOR R = nG

## Slide 28: Quiz 1 Parity Checking
Q: Compute the parity bits for the following data matrix:
  1 0 1
  0 1 0
  1 1 1
A:
  1 0 1 | 0
  0 1 0 | 1
  1 1 1 | 1
  ------------
  0 0 0 | 0
Q: Compute the parity bits for the following data matrix:
  1 0 1
  0 0 0
  1 0 1
A:
  1 0 1 |
  0 0 0 |
  1 0 1 |
  ------------
  |

## Slide 29: Quiz 2 Internet checksum
Q: Suppose that a packet 1001 1100 1010 0011 is transmitted using Internet checksum (N=4-bit integer). What is the value of the checksum?
A: One’s complement sum for 4-bit integers is defined as sum modulo 2N, N=4, and adding any overflow of high order bits back into low-order bits, then taking one’s complement.
0011+1010 = 1101
1101+1100 = 1001+1 = 1010
1010+1001 = 0011+1 = 0100.
So, the Internet checksum is 1011, the one’s complement of 0100.

## Slide 30: Quiz 3 CRC
Q: A bit stream 1001 is transmitted using the standard CRC method. The generator is 1011. Show the actual bit string transmitted. Suppose that the first bit sent is inverted during transmission error. Show that this error is detected at the receiver’s end. Give an example of bit errors in the bit string transmitted that will not be detected by the receiver.
A: D=1001, G=1011, r=3. Compute R
The message after appending three zeros is 1001000. The remainder on dividing 1001000 by 1011 is 110. So, the actual bits transmitted are 1001110.
The received bit stream with an error in the first bit is 0001110. Dividing this by 1011 produces a remainder of 101, which is different from 0. Thus, the receiver detects an error.
If the transmitted bit stream is converted to any multiple of 1001, the error will not be detected. A trivial example is if all ones in the bit stream are inverted to 0.

## Slide 31: Quiz 4 CRC
D=1001100, G=1011, r=3. Compute R
D=110011, G=1001, r=3. Compute R