## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 7 Wireless and
Mobile Networks
Acknowledgement: Based on the textbook’s website: https://gaia.cs.umass.edu/kurose_ross/index.php
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
lighter header font
4G/5G material completely updated; older 2/2.5/3G removed
8.2 (July 2023). Changes from 8.0:
minor updates and additional, including removing master/slave Bluetooth language
expansion, better graphics on wireless link characteristics
expanded, significant revisions of 4G/5G material (but not mobility)

## Slide 2: Chapter 7 outline
Introduction
Wireless
Wireless links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols

## Slide 3: What is mobility?
spectrum of mobility, from the network perspective:
no mobility
high mobility
device moves
between networks, but
powers down
while moving
device moves within same AP in
one provider
network
device moves
among multiple
provider networks,
while maintaining
ongoing connections
device moves among APs in
one provider
network
We’re interested in these!

## Slide 4: Mobility challenge:
If a device moves from one network another:
How will the “network” know to forward packets to the new network?
public Internet
AT&T
Verizon
client moves from Verizon to AT&T
datacenter
network
content
provider
network

## Slide 5: Mobility approaches
let network (routers) handle it:
  routers advertise well-known name, address (e.g., permanent 32-bit IP address), or number (e.g., cell #) of visiting mobile node via usual routing table exchange
  Internet routing could do this already with no changes! Routing tables indicate where each mobile located via longest prefix match!

## Slide 6: Mobility approaches
let network (routers) handle it:
  routers advertise well-known name, address (e.g., permanent 32-bit IP address), or number (e.g., cell #) of visiting mobile node via usual routing table exchange
  Internet routing could do this already with no changes! Routing tables indicate where each mobile located via longest prefix match!
let end-systems handle it: functionality at the “edge”
  indirect routing: communication from correspondent to mobile goes through home network, then forwarded to remote mobile
  direct routing: correspondent gets foreign address of mobile, send directly to mobile
not
scalable
to billions of
mobiles

## Slide 7: Contacting a mobile friend:
search all phone books?
expect her to let you know where he/she is?
I wonder where Alice moved to?
Consider friend frequently changing locations, how do you find him/her?
call his/her parents?
Facebook!
The importance of having a “home”:
a definitive source of information about you
a place where people can find out where you are

## Slide 8: Home network, visited network: 4G/5G
…
visited mobile
carrier network
…
public Internet
and
inter-carrier IPX
…
P-GW
P-GW
home mobile
carrier network
Home
Subscriber
Server
in home network
roaming in visited network
SIM card: global identify info including home network
home network:
(paid) service plan with cellular provider, e.g., Verizon, Orange
home network HSS stores identify & services info
visited network:
any network other than your home network
service agreement with other networks: to provide access to visiting mobile

## Slide 9: Home network, visited network: ISP/WiFi
…
…
public Internet
…
authentication
access
server
attach
attach
authentication
access
server
ISP/WiFi: no notion of global “home”
credentials from ISP (e.g., username, password) stored on device or with user
ISPs may have national, international presence
different networks: different credentials
  some exceptions (e.g., eduroam)
  architectures exist (mobile IP) for 4G-like mobility, but not used

## Slide 10: Home network, visited network: generic
Home gateway
Home Network
  e.g.,: 128.119/16
Home network gateway
Permanent IP:
128.119.40.186
IMSI
78:4f:43:98:d9:27
Visited network gateway
NAT IP:
10.0.0.99
IMSI
78:4f:43:98:d9:27
public or private Internet
Home
Subscriber
Server
Mobility manager
Mobility manager
Correspondent
Visited Network
e.g.,: 79.129/16

## Slide 11: Registration: home needs to know where you are!
Home gateway
Home network gateway
Permanent IP:
128.119.40.186
IMSI
78:4f:43:98:d9:27
Visited network gateway
NAT IP:
10.0.0.99
IMSI
78:4f:43:98:d9:27
public or private Internet
Home
Subscriber
Server
Mobility manager
Mobility manager
end result:
visited mobility manager knows about mobile
home HSS knows location of mobile
2
visited mobility manager registers mobile’s location with home HSS
mobile associates with visited mobility manager
1
Home Network
  e.g.,: 128.119/16
Visited Network
e.g.,: 79.129/16

## Slide 12: Mobility with indirect routing
Home gateway
Home network gateway
Permanent IP:
128.119.40.186
IMSI
78:4f:43:98:d9:27
Visited network gateway
NAT IP:
10.0.0.99
IMSI
78:4f:43:98:d9:27
public or private Internet
Home
Subscriber
Server
Mobility manager
Mobility manager
Correspondent
1
correspondent uses home address as datagram destination address
home gateway receives datagram, forwards (tunnels) to remote gateway
Home Network
  e.g.,: 128.119/16
Visited Network
e.g.,: 79.129/16
2
3
4a
4b
visited gateway router forwards to mobile
visited gateway router forwards reply to correspondent via home network (4a) or directly (4b)

## Slide 13: Mobility with indirect routing: comments
triangle routing:
  inefficient when correspondent and mobile are in same network
mobile moves among visited networks: transparent to correspondent!
  registers in new visited network
  new visited network registers with home HSS
  datagrams continue to be forwarded from home network to mobile in new network
  on-going (e.g., TCP) connections between correspondent and mobile can be maintained!

## Slide 14: Mobility with direct routing
Home gateway
Permanent IP:
128.119.40.186
IMSI
78:4f:43:98:d9:27
Visited network gateway
NAT IP:
10.0.0.99
IMSI
78:4f:43:98:d9:27
public or private Internet
Home
Subscriber
Server
Mobility manager
Mobility manager
Correspondent
1
correspondent contacts home HSS, gets mobile’s visited network
Home Network
  e.g.,: 128.119/16
Visited Network
e.g.,: 79.129/16
4
visited gateway router forwards to mobile
2
3
Correspondent addresses datagram to visited network address

## Slide 15: Mobility with direct routing: comments
overcomes triangle routing inefficiencies
non-transparent to correspondent: correspondent must get care-of-address from home agent
what if mobile changes visited network?
  can be handled, but with additional complexity

## Slide 16: Chapter 7 outline
Introduction
Wireless
Wireless links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols

## Slide 17: Mobility in 4G networks: major mobility tasks
Mobility manager
Visited network
P-GW
Streaming server
Home
network
Internet
base station
MME
1
2
3
4
Home
Subscriber
Server
S-GW
P-GW
base station association:
covered earlier
mobile provides IMSI – identifying itself, home network
1
control-plane configuration:
MME, home HSS establish control-plane state - mobile is in visited network
2
data-plane configuration:
MME configures forwarding tunnels for mobile
visited, home network establish tunnels from home P-GW to mobile
3
mobile handover:
mobile device changes its point of attachment to visited network
4

## Slide 18: Configuring LTE control-plane elements
Mobility manager
Mobile communicates with local MME via BS control-plane channel
MME uses mobile’s IMSI info to contact mobile’s home HSS
  retrieve authentication, encryption, network service information
  home HHS knows mobile now resident in visited network
BS, mobile select parameters for BS-mobile data-plane radio channel
Visited network
P-GW
Home
network
base station
MME
2
Home
Subscriber
Server
S-GW
P-GW

## Slide 19: Configuring data-plane tunnels for mobile
Mobility manager
P-GW
Streaming server
Internet
base station
MME
Home
Subscriber
Server
S-GW
P-GW
Visited network
Home
network
S-GW to BS tunnel: when mobile changes base stations, simply change endpoint IP address of tunnel
S-GW to home P-GW tunnel: implementation of indirect routing
tunneling via GTP (GPRS tunneling protocol): mobile’s datagram to streaming server encapsulated using GTP inside UDP, inside datagram

## Slide 20: Handover between BSs in same cellular network
P-GW
S-GW
MME
source BS
1
3
2
data path before handover
data path after
handover
1
current (source) BS selects target BS, sends Handover Request message to target BS
2
target BS pre-allocates radio time slots, responds with HR ACK with info for mobile
3
source BS informs mobile of new BS
mobile can now send via new BS - handover looks complete to mobile
4
source BS stops sending datagrams to mobile, instead forwards to new BS (who forwards to mobile over radio channel)
target BS
4

## Slide 21: Handover between BSs in same cellular network
1
6
3
5
5
2
5
target BS informs MME that it is new BS for mobile
MME instructs S-GW to change tunnel endpoint to be (new) target BS
6
target BS ACKs back to source BS: handover complete, source BS can release resources
P-GW
S-GW
MME
source BS
target BS
4
7
7
mobile’s datagrams now flow through new tunnel from target BS to S-GW

## Slide 22: Mobile IP
mobile IP architecture standardized ~20 years ago [RFC 5944]
  long before ubiquitous smartphones, 4G support for Internet protocols
  did not see wide deployment/use
  perhaps WiFi for Internet, and 2G/3G phones for voice were “good enough” at the time
mobile IP architecture:
  indirect routing to node (via home network) using tunnels
  mobile IP home agent: combined roles of 4G HSS and home P-GW
  mobile IP foreign agent: combined roles of 4G MME and S-GW
  protocols for agent discovery in visited network, registration of visited location in home network via ICMP extensions

## Slide 23: Wireless, mobility: impact on higher layer protocols
logically, impact should be minimal …
  best effort service model remains unchanged
  TCP and UDP can (and do) run over wireless, mobile
… but performance-wise:
  packet loss/delay due to bit-errors (discarded packets, delays for link-layer retransmissions), and handover loss
  TCP interprets loss as congestion, will decrease congestion window un-necessarily
  delay impairments for real-time traffic
  bandwidth a scare resource for wireless links

## Slide 24: Chapter 7 summary
Wireless
Wireless Links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols