## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 5 Network Layer:
Control Plane
Acknowledgement: Based on the textbook’s website: https://gaia.cs.umass.edu/kurose_ross/index.php
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
lighter header font
Re-do of network management slides; redo of Bellman-Ford slides
8.2 (changes over 8.0)
improved animations of Dijkstra’s algorithm and Bellman Ford
various improvements to BGP
SDN: added Google Orion (2021 Google network SDN control plane)

## Slide 2: Network layer control plane: our goals
understand principles behind network control plane:
  traditional routing algorithms
  SDN controllers
  network management, configuration
instantiation, implementation in the Internet:
  OSPF, BGP
  OpenFlow, ODL and ONOS controllers
  Internet Control Message Protocol: ICMP
  SNMP, YANG/NETCONF

## Slide 3: Network layer: “control plane” roadmap
network management, configuration
  SNMP
  NETCONF/YANG
introduction
routing protocols
  link state
  distance vector
intra-ISP routing: OSPF
routing among ISPs: BGP
SDN control plane
Internet Control Message Protocol

## Slide 4: Network-layer functions
Two approaches to structuring network control plane:
per-router control (traditional)
logically centralized control (software defined networking)
forwarding: move packets from router’s input to appropriate router output
data plane
control plane
routing: determine route taken by packets from source to destination
IMPORTANT

## Slide 5: Per-router control plane
Individual routing algorithm components in each and every router interact in the control plane
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header
3
IMPORTANT

## Slide 6: Software-Defined Networking (SDN) control plane
Remote controller computes, installs forwarding tables in routers
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header
IMPORTANT

## Slide 7: Per-router control plane
SDN control plane
IMPORTANT

## Slide 8: Network layer: “control plane” roadmap
network management, configuration
  SNMP
  NETCONF/YANG
introduction
routing protocols
  link state
  distance vector
intra-ISP routing: OSPF
routing among ISPs: BGP
SDN control plane
Internet Control Message Protocol

## Slide 9: Routing protocols
Routing protocol goal: determine “good” paths (equivalently, routes), from sending hosts to receiving host, through network of routers
path: sequence of routers packets traverse from given initial source host to final destination host
“good”: least “cost”, “fastest”, “least congested”
routing: a “top-10” networking challenge!
mobile network
enterprise
network
national or global ISP
datacenter
network
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
IMPORTANT

## Slide 10: Graph abstraction: link costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
ca,b: cost of direct link connecting a and b
e.g., cw,z = 5, cu,z = ∞
  cost defined by network operator: could always be 1, or inversely related to bandwidth, or inversely related to congestion
N: set of routers = { u, v, w, x, y, z }
E: set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
IMPORTANT

## Slide 11: Routing algorithm classification
global or decentralized information?
global: all routers have complete topology, link cost info
“link state” algorithms
decentralized: iterative process of computation, exchange of info with neighbors
routers initially only know link costs to attached neighbors
“distance vector” algorithms
How fast do routes change?
dynamic: routes change more quickly
  periodic updates or in response to link cost changes
static: routes change slowly over time
IMPORTANT

## Slide 12: Network layer: “control plane” roadmap
network management, configuration
  SNMP
  NETCONF/YANG
introduction
routing protocols
  link state
  distance vector
intra-ISP routing: OSPF
routing among ISPs: BGP
SDN control plane
Internet Control Message Protocol

## Slide 13: Dijkstra’s link-state routing algorithm
centralized: network topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
computes least cost paths from one node (“source”) to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k destinations
cx,y: direct link cost from node x to y; = ∞ if not direct neighbors
D(v): current estimate of cost of least-cost-path from source to destination v
p(v): predecessor node along path from source to v
N': set of nodes whose least-cost-path definitively known
notation
IMPORTANT

## Slide 14: Dijkstra’s link-state routing algorithm
1 Initialization:
2 N' = {u} /* compute least cost path from u to all other nodes */
3 for all nodes v
4 if v adjacent to u /* u initially knows direct-path-cost only to direct neighbors */
5 then D(v) = cu,v /* but may not be minimum cost! */
6 else D(v) = ∞
7
8 Loop
9
10
11
12
13
14
15 until all nodes in N'
find w not in N' such that D(w) is a minimum
add w to N'
update D(v) for all v adjacent to w and not in N' :
D(v) = min ( D(v), D(w) + cw,v )
/* new least-path-cost to v is either old least-cost-path to v or known
least-cost-path to w plus direct-cost from w to v */
IMPORTANT

## Slide 15: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
D(w),p(w)
5,u
4,x
3,y
3,y
5,u
∞
∞
1,u
2,u
u
v
w
x
y
z
Initialization (step 0):
For all a: if a adjacent to u then D(a) = cu,a
IMPORTANT

## Slide 16: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
D(w),p(w)
5,u
4,x
3,y
3,y
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
IMPORTANT

## Slide 17: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
D(w),p(w)
5,u
4,x
3,y
3,y
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
11
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
∞
2,x
4,x
2,u
D(v) = min ( D(v), D(x) + cx,v ) = min(2, 1+2) = 2
D(w) = min ( D(w), D(x) + cx,w ) = min (5, 1+3) = 4
D(y) = min ( D(y), D(x) + cx,y ) = min(inf,1+1) = 2
IMPORTANT

## Slide 18: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
D(w),p(w)
5,u
4,x
3,y
3,y
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
IMPORTANT

## Slide 19: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
11
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
4,y
3,y
2,u
D(w) = min ( D(w), D(y) + cy,w ) = min (4, 2+1) = 3
D(z) = min ( D(z), D(y) + cy,z ) = min(inf,2+2) = 4
IMPORTANT

## Slide 20: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
4,y
3,y
2,u
uxyv
IMPORTANT

## Slide 21: Dijkstra’s algorithm: an example
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
D(w) = min ( D(w), D(v) + cv,w ) = min (3, 2+3) = 3
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
11
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
4,y
3,y
2,u
uxyv
4,y
3,y
IMPORTANT

## Slide 22: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
4,y
3,y
2,u
uxyv
4,y
3,y
uxyvw
IMPORTANT

## Slide 23: Dijkstra’s algorithm: an example
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
D(z) = min ( D(z), D(w) + cw,z ) = min (4, 3+5) = 4
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
11
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
4,y
3,y
2,u
uxyv
4,y
3,y
uxyvw
4,y
IMPORTANT

## Slide 24: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
4,y
3,y
2,u
uxyv
4,y
3,y
uxyvw
4,y
uxyvwz
IMPORTANT

## Slide 25: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
D(w),p(w)
5,u
∞
∞
1,u
2,u
u
8 Loop
9
10
11
find a not in N' such that D(a) is a minimum
add a to N'
ux
v
w
x
y
z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
∞
2,x
4,x
2,u
uxy
4,y
3,y
2,u
uxyv
4,y
3,y
uxyvw
4,y
uxyvwz
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
IMPORTANT

## Slide 26: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
4,y
D(w),p(w)
D(w),p(w)
5,u
4,x
3,y
3,y
4,y
3,y
5,u
∞
∞
1,u
2,u
∞
2,x
4,x
2,u
4,y
3,y
2,u
uxyvwz
uxyvw
uxyv
uxy
ux
u
v
w
x
y
z
find a not in N' such that D(a) is a minimum
add a to N'
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
Initialization (step 0): For all a: if a adjacent to then D(a) = cu,a
IMPORTANT

## Slide 27: Dijkstra’s algorithm: an example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
5,u
4,x
3,y
3,y
u
y
x
w
v
z
resulting least-cost-path tree from u:
resulting forwarding table in u:
v
x
y
w
x
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
outgoing link
route from u to v directly
route from u to all other destinations via x
IMPORTANT

## Slide 28: Dijkstra’s algorithm: another example
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Step
N'
D(v),
p(v)
0
1
2
3
4
5
D(w),
p(w)
D(x),
p(x)
D(y),
p(y)
D(z),
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
notes:
construct least-cost-path tree by tracing predecessor nodes
ties can exist (can be broken arbitrarily)
uwxvyz
v
w
x
y
z
IMPORTANT

## Slide 29: Dijkstra’s algorithm: discussion
algorithm complexity: n nodes
each of n iteration: need to check all nodes, w, not in N
n(n+1)/2 comparisons: O(n2) complexity
more efficient implementations possible: O(nlogn)
message complexity:
each router must broadcast its link state information to other n routers
efficient (and interesting!) broadcast algorithms: O(n) link crossings to disseminate a broadcast message from one source
each router’s message crosses O(n) links: overall message complexity: O(n2)
IMPORTANT

## Slide 30: Network layer: “control plane” roadmap
network management, configuration
  SNMP
  NETCONF/YANG
introduction
routing protocols
  link state
  distance vector
intra-ISP routing: OSPF
routing among ISPs: BGP
SDN control plane
Internet Control Message Protocol

## Slide 31: Dijkstra's Algorithm vs. Bellman-Ford Algorithm
Dijkstra's Algorithm:
  Uses a priority queue to select the next vertex to process.
  Greedily selects the vertex with the smallest tentative distance to source node.
  Works only on graphs with non-negative edge weights.
Bellman-Ford Algorithm:
  Iteratively relaxes all edges V-1 times, where V is the number of vertices.
  Does not use a priority queue.
  Can handle graphs with negative edge weights, and can detect negative cycles.
Dijkstra's algorithm is faster and more efficient for graphs with non-negative weights, the Bellman-Ford algorithm is more versatile as it can handle negative weights and detect negative cycles, albeit at the cost of lower efficiency.
Notes: Dijkstra's Algorithm:
- Finds the shortest path from a single source vertex to all other vertices in a graph with non-negative edge weights.
**Bellman-Ford Algorithm:**
- Finds the shortest path from a single source vertex to all other vertices in a graph, even with negative edge weights.
- Can detect negative cycles in the graph.
## Edge Weight Handling
**Dijkstra's Algorithm:**
- Works only on graphs with non-negative edge weights.
**Bellman-Ford Algorithm:**
- Can handle graphs with negative edge weights.
- Can detect negative cycles.
## Performance
Dijkstra's Algorithm:
- More efficient for graphs with non-negative weights.
- Time complexity: O(V log V + E) with a binary heap implementation, where V is the number of vertices and E is the number of edges.
**Bellman-Ford Algorithm:**
- Generally slower than Dijkstra's.
- Time complexity: O(VE), where V is the number of vertices and E is the number of edges.
## Implementation

## Slide 32: Distance vector algorithm
Based on Bellman-Ford (BF) equation (dynamic programming):
Let Dx(y): cost of least-cost path from x to y.
Then:
Dx(y) = minv { cx,v + Dv(y) }
Bellman-Ford equation
min taken over all neighbors v of x
v’s estimated least-cost-path cost to y
direct cost of link from x to v

## Slide 33: Bellman-Ford Algorithm
Each router maintains a Distance Vector table containing the distance between itself and All possible destination nodes. Distances, based on a chosen metric, are computed using information from the neighbors’ distance vectors.
Information kept by DV router:
  Each router has an ID
  Associated with each link connected to a router, there is a link cost (static or dynamic).
  Intermediate hops
Distance Vector Table Initialization:
  Distance to itself = 0
  Distance to ALL other routers = infinity number.

## Slide 34: The DV Algorithm
A router transmits its distance vector to each of its neighbors in a routing packet.
Each router receives and saves the most recently received distance vector from each of its neighbors.
A router recalculates its distance vector when:
  It receives a distance vector from a neighbor containing different information than before.
  It discovers that a link to a neighbor has gone down.
The DV calculation is based on minimizing the cost to each destination
Dx(y) = Estimate of least cost from x to y
C(x,v) = Node x knows cost to each neighbor v
Dx = [Dx(y): y ? N ] = Node x maintains distance vector
Node x also maintains its neighbors' distance vectors
– For each neighbor v, x maintains Dv = [Dv(y): y ? N ]

## Slide 35
From time-to-time, each node sends its own distance vector estimate to neighbors.
When a node x receives new DV estimate from any neighbor v, it saves v’s distance vector and it updates its own DV using B-F equation:

## Slide 36: Bellman-Ford Example
u
y
z
2
2
1
3
1
1
2
5
3
5
Suppose that u’s neighboring nodes, x,v,w, know that for destination z:
Du(z) = min { cu,v + Dv(z),
cu,x + Dx(z),
cu,w + Dw(z) }
Bellman-Ford equation says:
Dv(z) = 5
v
Dw(z) = 3
w
Dx(z) = 3
x
= min {2 + 5,
1 + 3,
5 + 3} = 4
node achieving minimum (x) is next hop on estimated least-cost path to destination (z)

## Slide 37: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)
Dx(y) ← minv{cx,v + Dv(y)} for each node y ∊ N
when x receives new DV estimate from any neighbor, it updates its own DV using B-F equation:

## Slide 38: Distance vector algorithm:
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
wait for (change in local link cost or msg from neighbor)
each node:
distributed, self-stopping: each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors – only if necessary
  no notification received, no actions taken!
recompute DV estimates using DV received from neighbor
if DV to any destination has changed, notify neighbors

## Slide 39: Distance vector: example
DV in a: Da(a)=0
Da(b) = 8
Da(c) = ∞
Da(d) = 1
Da(e) = ∞
Da(f) = ∞
Da(g) = ∞
Da(h) = ∞
Da(i) = ∞
g
h
i
1
1
1
1
1
1
1
1
1
8
1
t=0
All nodes have distance estimates to nearest neighbors (only)
A few asymmetries:
missing link
larger cost
d
e
f
a
b
c
All nodes send their local distance vector to their neighbors

## Slide 40: Distance vector example: iteration
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=1
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c

## Slide 41: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=1
compute
compute
compute
compute
compute
compute
compute
compute
compute

## Slide 42: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=1

## Slide 43: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=2

## Slide 44: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
8
1
2
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=2
compute
compute
compute
compute
compute
compute
compute
compute
compute

## Slide 45: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=2

## Slide 46: Distance vector example: iteration
…. and so on
Let’s next take a look at the iterative computations at nodes

## Slide 47: Distance vector example: computation
DV in a: Da(a)=0
Da(b) = 8
Da(c) = ∞
Da(d) = 1
Da(e) = ∞
Da(f) = ∞
Da(g) = ∞
Da(h) = ∞
Da(i) = ∞
g
h
i
1
1
1
1
1
1
1
1
1
8
1
t=1
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
b receives DVs from a, c, e
a
b
c
d
e
f
DV in c:
  Dc(a) = ∞
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = ∞
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
DV in e:
  De(a) = ∞
  De(b) = 1
  De(c) = ∞
  De(d) = 1
  De(e) = 0
  De(f) = 1
  De(g) = ∞
  De(h) = 1
De(i) = ∞

## Slide 48: Distance vector example: computation
DV in a: Da(a)=0
Da(b) = 8
Da(c) = ∞
Da(d) = 1
Da(e) = ∞
Da(f) = ∞
Da(g) = ∞
Da(h) = ∞
Da(i) = ∞
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
DV in c:
  Dc(a) = ∞
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = ∞
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
DV in e:
  De(a) = ∞
  De(b) = 1
  De(c) = ∞
  De(d) = 1
  De(e) = 0
  De(f) = 1
  De(g) = ∞
  De(h) = 1
De(i) = ∞
g
h
i
1
1
1
1
1
1
1
1
1
8
1
t=1
b receives DVs from a, c, e, computes:
a
b
c
d
e
f
DV in b:
Db(f) =2
Db(g) = ∞
Db(h) = 2
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = 2
  Db(e) = 1
e
compute
b
Db(a) = min{cb,a+Da(a), cb,c +Dc(a), cb,e+De(a)} = min{8,∞,∞} = 8
Db(c) = min{cb,a+Da(c), cb,c +Dc(c), c b,e +De(c)} = min{∞,1,∞} = 1
Db(d) = min{cb,a+Da(d), cb,c +Dc(d), c b,e +De(d)} = min{9,2,∞} = 2
Db(f) = min{cb,a+Da(f), cb,c +Dc(f), c b,e +De(f)} = min{∞,∞,2} = 2
Db(i) = min{cb,a+Da(i), cb,c +Dc(i), c b,e+De(i)} = min{∞, ∞, ∞} = ∞
Db(h) = min{cb,a+Da(h), cb,c +Dc(h), c b,e+De(h)} = min{∞, ∞, 2} = 2
Db(e) = min{cb,a+Da(e), cb,c +Dc(e), c b,e +De(e)} = min{∞,∞,1} = 1
Db(g) = min{cb,a+Da(g), cb,c +Dc(g), c b,e+De(g)} = min{∞, ∞, ∞} = ∞

## Slide 49: Distance vector example: computation
DV in a: Da(a)=0
Da(b) = 8
Da(c) = ∞
Da(d) = 1
Da(e) = ∞
Da(f) = ∞
Da(g) = ∞
Da(h) = ∞
Da(i) = ∞
g
h
i
1
1
1
1
1
1
1
1
1
8
1
t=1
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
c receives DVs from b
a
b
c
d
e
f
DV in c:
  Dc(a) = ∞
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = ∞
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
DV in e:
  De(a) = ∞
  De(b) = 1
  De(c) = ∞
  De(d) = 1
  De(e) = 0
  De(f) = 1
  De(g) = ∞
  De(h) = 1
De(i) = ∞

## Slide 50: Distance vector example: computation
g
h
i
1
1
8
1
t=1
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
c receives DVs from b computes:
a
b
c
d
e
f
DV in c:
  Dc(a) = ∞
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = ∞
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
Dc(a) = min{cc,b+Db(a}} = 1 + 8 = 9
Dc(b) = min{cc,b+Db(b)} = 1 + 0 = 1
Dc(d) = min{cc,b+Db(d)} = 1+ ∞ = ∞
Dc(e) = min{cc,b+Db(e)} = 1 + 1 = 2
Dc(f) = min{cc,b+Db(f)} = 1+ ∞ = ∞
Dc(g) = min{cc,b+Db(g)} = 1+ ∞ = ∞
Dc(i) = min{cc,b+Db(i)} = 1+ ∞ = ∞
Dc(h) = min{cbc,b+Db(h)} = 1+ ∞ = ∞
DV in c:
  Dc(a) = 9
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = 2
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
compute
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 51: Distance vector example: computation
1
1
1
1
1
1
1
1
1
8
1
t=1
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
e receives DVs from b, d, f, h
a
b
c
DV in f:
  Dc(a) = ∞
  Dc(b) = ∞
  Dc(c) = ∞
  Dc(d) = ∞
  Dc(e) = 1
  Dc(f) = 0
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = 1
DV in e:
  De(a) = ∞
  De(b) = 1
  De(c) = ∞
  De(d) = 1
  De(e) = 0
  De(f) = 1
  De(g) = ∞
  De(h) = 1
De(i) = ∞
DV in h:
  Dc(a) = ∞
  Dc(b) = ∞
  Dc(c) = ∞
  Dc(d) = ∞
  Dc(e) = 1
  Dc(f) = ∞
  Dc(g) = 1
  Dc(h) = 0
Dc(i) = 1
DV in d:
  Dc(a) = 1
  Dc(b) = ∞
  Dc(c) = ∞
  Dc(d) = 0
  Dc(e) = 1
  Dc(f) = ∞ Dc(g) = 1
  Dc(h) = ∞
Dc(i) = ∞
d
e
f
g
h
i
Q: what is new DV computed in e at t=1?
compute

## Slide 52: Distance vector: state information diffusion
t=0
c’s state at t=0 is at c only
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
c’s state at t=0 has propagated to b, and may influence distance vector computations up to 1 hop away, i.e., at b
t=1
c’s state at t=0 may now influence distance vector computations up to 2 hops away, i.e., at b and now at a, e as well
t=2
c’s state at t=0 may influence distance vector computations up to 3 hops away, i.e., at d, f, h
t=3
c’s state at t=0 may influence distance vector computations up to 4 hops away, i.e., at g, i
t=4
Iterative communication, computation steps diffuses information through network:
t=1
t=2
t=3
t=4

## Slide 53: Distance vector: another example
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
Dx()
Dx(y) = min{cx,y + Dy(y), cx,z+ Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{cx,y+ Dy(z), cx,z+ Dz(z)}
= min{2+1 , 7+0} = 3
3
2
Dy()
Dz()
cost to
from

## Slide 54: Distance vector: another example
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
cost to
from
from
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
x
z
1
2
7
y
Dx()
Dy()
Dz()
from
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
from
x y z
x
y
z
0
2 0 1
7 1 0
3
2
cost to
time

## Slide 55: Distance vector: link cost changes
“good news
travels fast”
t0 : y detects link-cost change, updates its DV, informs its neighbors.
t1 : z receives update from y, updates its DV, computes new least cost to x , sends its neighbors its DV.
t2 : y receives z’s update, updates its DV. y’s least costs do not change, so y does not send a message to z.
link cost changes:
node detects local link cost change
updates routing info, recalculates local DV
if DV changes, notify neighbors
x
z
1
4
50
y
1

## Slide 56: Comparison of LS and DV algorithms
message complexity
  LS: n routers, O(n2) messages sent
  DV: exchange between neighbors; convergence time varies
speed of convergence
LS: O(n2) algorithm, O(n2) messages
  may have oscillations
DV: convergence time varies
  may have routing loops
  count-to-infinity problem
robustness: what happens if router malfunctions, or is compromised?
LS:
  router can advertise incorrect link cost
  each router computes only its own table
DV:
  DV router can advertise incorrect path cost (“I have a really low-cost path to everywhere”): black-holing
  each router’s DV is used by others: error propagate thru network