## Slide 1
Midterm Exam 2024 Questions (Selected)
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Notes: (8.2)Version
7.2 (January 2020)
All slides reformatted for 16:9 aspect ratio
Use of Calibri font, rather that Gill Sans MT
Updated slide content for 2020 link technologies and applications
Add more animation throughout
New Master slide
Feb. 2020 (8.0)
a few updates suggest by Catherine Rosenberg (thanks!)
titles in a lighter font
Sept 2020 (8.1)
Added ~7 new slides, in particular: data center slide; routing versus forwarding; security line of defense; several on encapsulation and layers (this section is a lot better now). Other relative minor changes throughout
Feb. 2023 (8.2)
few minor updates (mostly speeds, technology details)

## Slide 2: Question 1.3-1 1.3-3
1.3-1 Routing versus forwarding. Choose one of the following two definitions that makes the correct distinction between routing versus forwarding.
ANS: Forwarding is the local action of moving arriving packets from router’s input link to appropriate router output link, while routing is the global action of determining the source-destination paths taken by packets.
1.3-3 Packet switching versus circuit switching (2). Which of the characteristics below are associated with the technique of circuit switching? Select all correct answers. [Hint: more than one of the answers is correct].
ANS: Reserves resources needed for a call from source to destination.
Frequency Division Multiplexing (FDM) and Time Division Multiplexing (TDM) are two approaches for implementing this technique.

## Slide 3: Question 1.4-01
1.4-01 Components of packet delay. Match the description of each component of packet delay to its name in the pull down list.

## Slide 4: Chapter 1: roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models

## Slide 5: How do packet delay and loss occur?
packets queue in router buffers, waiting for turn for transmission
  queue length grows when arrival rate to link (temporarily) exceeds output link capacity
packet loss occurs when memory to hold queued packets fills up
A
B
packet being transmitted (transmission delay)
packets in buffers (queueing delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers
IMPORTANT

## Slide 6: Packet delay: four sources
dproc: nodal processing
check bit errors
determine output link
typically < microsecs
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
IMPORTANT

## Slide 7: Packet delay: four sources
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
dtrans: transmission delay:
L: packet length (bits)
R: link transmission rate (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different
IMPORTANT

## Slide 8: Throughput
throughput: rate (bits/time unit) at which bits are being sent from sender to receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
(Rs bits/sec)
pipe that can carry
fluid at rate
(Rc bits/sec)
IMPORTANT

## Slide 9: Throughput
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec
IMPORTANT

## Slide 10: Throughput: network scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
Link utilization: used bandwidth/available bandwidth. For the three links:
  min(Rc,Rs,R/10)/Rs
  min(Rc,Rs,R/10)/(R/10)
  min(Rc,Rs,R/10)/Rc
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/
IMPORTANT

## Slide 11: Question 1.4-01a
1.4-01a. Performance: Delay. Consider the network shown in the figure below, with three links, each with a transmission rate of 1 Mbps, and a propagation delay of 1 msec per link. Assume the length of a packet is 1000 bits.
What is the end-end delay of a packet from when it first begins transmission on link 1, until is it received in full by the server at the end of link 3. You can assume that queueing delays and packet processing delays are zero, but make sure you include packet transmission time delay on all links. Assume store-and forward packet transmission.
Each link has transmission delay 1000 bits/1 Mbps = 1ms. So each link has total delay of transmission + propagation = 1+1=2 ms.
For the three links, the total delay = 2 + 2 + 2 = 6 ms. `

## Slide 12: Question 1.4-01b
Maximum end-end throughput. Consider the scenario shown below, with a single source client sending to a server over two links of capacities R1=100 Mbps and R3=10 Mbps.
What is the maximum achievable end-end throughput (in Mbps, give an integer value) for the client-to-server pair, assuming that the client is trying to send at its maximum rate?
min (R1, R3) = min (100, 10) = 10 Mpbs.

## Slide 13: Question 1.4-01c
Performance: Maximum end-end throughput. Consider the scenario shown below, with a single source client sending to a server over two links of capacities R1=10 Mbps and R3=100 Mbps.
What is the maximum achievable end-end throughput (in Mbps, give an integer value) for the client-to-server pair, assuming that the client is trying to send at its maximum rate?
min (R1, R3) = min (10, 100) = 10 Mpbs.

## Slide 14: Question 1.4-01c
Performance: Maximum end-end throughput. Consider the scenario shown below, with a single source client sending to a server over two links of capacities R1=10 Mbps and R3=100 Mbps.
What is the maximum achievable end-end throughput (in Mbps, give an integer value) for the client-to-server pair, assuming that the client is trying to send at its maximum rate?
min (R1, R3) = min (10, 100) = 10 Mpbs.

## Slide 15: Question 1.4-01d
1.4-01e. Performance: Maximum end-end throughput. Consider the scenario shown below, with two clients sending to a server. The links attached to clients each have a capacity of R1= R2 = 100 Mbps. The link from the router to the server has a capacity of and R3 = 10 Mbps, which is shared evenly between the two sources when they are each sending at their maximum rate.
What is the maximum achievable end-end throughput (in Mbps, give an integer value) for each client-to-server pair, assuming that the client is trying to send at its maximum rate?
The maximum achievable end-end throughput is min (R1, R3/2) = min (R2, R3/2) = min (100, 10/2) = 5 Mbps.
The shared 100 Mbps link is fairly shared among two end-to-end connections (R1, R3) and (R2, R3), hence each end-to-end connection gets 10/2=5 Mbps.
100 Mbps
100 Mbps
10 Mbps
Notes: The link bandwidth is independent of the transmission direction.

## Slide 16: Question 1.4-01e
1.4-01e. Performance: Maximum end-end throughput. Consider the scenario shown below, with two clients sending to a server. The links attached to clients each have a capacity of R1= R2 = 10 Mbps. The link from the router to the server has a capacity of and R3 = 100 Mbps, which is shared evenly between the two sources when they are each sending at their maximum rate.
What is the maximum achievable end-end throughput (in Mbps, give an integer value) for each client-to-server pair, assuming that the client is trying to send at its maximum rate?
The maximum achievable end-end throughput is min (R1, R3/2) = min (R2, R3/2) = min (10, 100/2) = 10 Mbps.
The shared 100 Mbps link is fairly shared among two end-to-end connections (R1, R3) and (R2, R3), hence each end-to-end connection gets 100/2=50 Mbps.
Note that min (R1, R2, R3/2) is incorrect, since R1 and R2 are on deferent end-to-end connections.
Remember that parallel links should never be put into the min() formula, only sequential links forming the same end-to-end connection should be in the same min() formula.
10 Mbps
10 Mbps
100 Mbps
Notes: The link bandwidth is independent of the transmission direction.

## Slide 17: Question 1.4-01e variations
1.4-01e. Performance: Maximum end-end throughput. Consider the scenario shown below, with two clients sending to a server. The links attached to clients each have a capacity of R1 = 10 Mbps, R2 = 20 Mbps. The link from the router to the server has a capacity of and R3 = 100 Mbps, which is shared evenly between the two sources when they are each sending at their maximum rate.
What is the maximum achievable end-end throughput (in Mbps, give an integer value) for each client-to-server pair, assuming that the client is trying to send at its maximum rate?
For client on top, the maximum achievable end-end throughput is min (R1, R3/2) = min (10, 100/2) = 10 Mbps.
For client on bottom, the maximum achievable end-end throughput is min (R1, R3/2) = min (20, 100/2) = 20 Mbps.
The shared 100 Mbps link is fairly shared among two end-to-end connections (R1, R3) and (R2, R3), hence each end-to-end connection gets 100/2=50 Mbps.
10 Mbps
20 Mbps
100 Mbps
Notes: The link bandwidth is independent of the transmission direction.

## Slide 18: Question 1.4-02a
Consider the scenario shown in Figure 1 in which a server is connected to a router by a 100Mbps link with a 50ms propagation delay. Initially this router is also connected to two routers, each over a 50Mbps link with a 200ms propagation delay. A 1Gbps link connects a host and a cache (if present) to each of these routers and we assume that this link has 0 propagation delay. All packets in the network are 20,000 bits long.
What is the end-­to­‐end delay (in msec) from when a packet is transmitted by the server to when it is received by the client? In this case, we assume there are no caches, there’s no queuing delay at the routers, and the packet processing delays at routers and nodes are all 0.
ANS: If all packets are 20,000 bits long it takes 200 usec to send the packet over the 100Mbps link, 400 usec to send over the 50Mbps link, and 20 usec to send over the 1Gbps link.
Sum of the three-link transmission is 620 usec. Thus, the total end-to-end delay is 250 ms + 620 usec = 250.62 msec.

## Slide 19: Question 1.4-02b
Here we assume that client hosts send requests for files directly to the server (caches are not used or off in this case). What is the maximum rate at which the server can deliver data to a single client if we assume no other clients are making requests?
Server can send at the max of the bottleneck link bandwidth min(100/2 Mbps, 50 Mbps, 1 Gbps) = 50 Mbps, since the top link is shared and the other two links are separate for each client and not shared.
Suppose we had 10 clients on the bottom, then the bottleneck link bandwidth min(100/10 Mbps, 50 Mbps, 1 Gbps) = 10 Mbps.

## Slide 20: Question 1.4-02c
Again we assume only one active client but in this case the caches are on and behave like HTTP caches. A client’s HTTP GET is always first directed to its local cache. 60% of the requests can be satisfied by the local cache. What is the average rate at which the client can receive data in this case?
60% of the requests can be satisfied by the local cache, with bandwidth of 1 Gbps = 1000 Mpbs.
40% of the requests go to the remote server, with bandwidth of min (100 Mbps, 50 Mbps, 1Gbps) = 50 Mpbs.
  Since we assume only one active client, we do not have 100/2 as the first term.
The average rate at which the client can receive data is .4*50+.6*1000=620 Mbps

## Slide 21: Question 1.4-02d
Now clients in both LANs are active and the both caches are on. 60% of the requests can be satisfied by the local caches. What is the average rate at which each client can receive data?
60% of the requests can be satisfied by the local cache, with bandwidth of 1 Gbps = 1000 Mpbs.
40% of the requests go to the remote server, with bandwidth of min (100/2 Mbps, 50 Mbps, 1Gbps) = 50 Mpbs.
  Since we both clients are active, we have 100/2 as the first term.
The average rate at which the client can receive data is .4*50+.6*1000=620 Mbps

## Slide 22: Client/server socket interaction: TCP
server (running on hostid)
client
wait for incoming
connection request
connectionSocket =
serverSocket.accept()
create socket,
port=x, for incoming request:
serverSocket = socket()
create socket,
connect to hostid, port=x
clientSocket = socket()
send request using
clientSocket
read request from
connectionSocket
write reply to
connectionSocket
TCP
connection setup
close
connectionSocket
read reply from
clientSocket
close
clientSocket
IMPORTANT

## Slide 23: Example app: TCP client
from socket import *
serverName = 'servername'
serverPort = 12000
clientSocket = socket(AF_INET, SOCK_STREAM)
clientSocket.connect((serverName,serverPort))
sentence = input('Input lowercase sentence:')
clientSocket.send(sentence.encode())
modifiedSentence = clientSocket.recv(1024)
print ('From Server:', modifiedSentence.decode())
clientSocket.close()
Python TCPClient
create TCP socket for server, remote port 12000
No need to attach server name, port
Note: this code update (2023) to Python 3
IMPORTANT

## Slide 24: Example app: TCP server
from socket import *
serverPort = 12000
serverSocket = socket(AF_INET,SOCK_STREAM)
serverSocket.bind(('',serverPort))
serverSocket.listen(1)
print('The server is ready to receive')
while True:
connectionSocket, addr = serverSocket.accept()
sentence = connectionSocket.recv(1024).decode()
capitalizedSentence = sentence.upper()
connectionSocket.send(capitalizedSentence.
encode())
connectionSocket.close()
Python TCPServer
create TCP welcoming socket
server begins listening for incoming TCP requests
loop forever
server waits on accept() for incoming requests, new socket created on return
read bytes from socket (but not address as in UDP)
close connection to this client (but not welcoming socket)
Note: this code update (2023) to Python 3
IMPORTANT

## Slide 25: Question 2.7-4
2.7-4 How many sockets? Suppose a Web server has five ongoing connections that use TCP receiver port 80, and assume there are no other TCP connections (open or being opened or closed) at that server. How many TCP sockets are in use at this server?
ANS: 6.
1 serverSocket and 5 connectionSockets

## Slide 26: Question 3.2-01
3.2-01. UDP multiplexing and demultiplexing. Consider the figure below, with 6 sockets shown across the network, and the corresponding Python code at each host. There are four UDP segments in flight. Match the source and destination port numbers for each segment with a value below.

## Slide 27: Question 3.2-04
3.2-04. TCP demultiplexing. Which of the following datagram and segment header fields are used, when demultiplexing data up to a TCP socket?
ANS: Source and destination IP addresses, and source and destination port numbers.

## Slide 28: Question 3.2-05
3.2-05a. TCP multiplexing/demultiplexing and connection management. Consider the scenario in the figure below, with two client hosts – client A (with one TCP socket) and client B (with two TCP sockets) exchanging packets with server B (with three TCP sockets). The Python code that created the three sockets on the server and the TCP code that created the one socket at the left client is shown in the diagram, with lines indicating the line of executed Python code that created each of the sockets. Which of the packets a, b, c, d have destination port 80?
ANS: Packets b, c and d
Notes: https://www.perplexity.ai/search/connection-oriented-demultiple-DayrDmqiStCQCLRRjqS30w

## Slide 29: Internet checksum
sender:
treat contents of UDP segment (including UDP header fields and IP addresses) as sequence of 16-bit integers
checksum: addition of segment content, then flip all the bits (one’s complement sum)
checksum value put into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  not equal - error detected
  equal - no error detected. But maybe errors nonetheless? More later ….
Goal: detect errors (i.e., flipped bits) in transmitted segment
IMPORTANT

## Slide 30: Internet checksum: an example
example: add two 16-bit integers
sum
checksum
Note: when adding numbers, a carryout from the most significant bit needs to be added to the result
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
IMPORTANT

## Slide 31: Internet checksum: weak protection!
example: add two 16-bit integers
sum
checksum
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
0 1
1 0
Even though numbers have changed (bit flips), no change in checksum!
IMPORTANT

## Slide 32: Question 3.3-1
3.3-1. Internet Checksum. Consider the two sixteen bit numbers: 10110100 01000110 01001000 01101111 Compute the Internet Checksum of these two values Enter the 2 bytes each as an 8-bit number with only 0’s and 1’s, and make a single blank space between the two 8-bit numbers (e.g., 01010101 00101000).
ANS: adding up the two numbers we have: 11111100 10110101
Taking ones complement we have: 00000011 01001010

## Slide 33: Router architecture overview
high-level view of generic router architecture:
high-speed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operates in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame
IMPORTANT

## Slide 34: Question 4.2-1
4.2-1. What's inside a router? Match the names of the principal router components (A,B,C,D below) with their function and whether they are in the network-layer data plane or control plane.

## Slide 35: Input port functions
switch
fabric
line
termination
physical layer:
bit-level reception
link
layer
protocol
(receive)
link layer:
e.g., Ethernet
(chapter 6)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
input port queuing: if datagrams arrive faster than forwarding rate into switch fabric
Frame
Datagram
IMPORTANT
Notes: Green box is a physical layer responsible for receiving bit level transmission. Copper, fiber wireless.
Link layer in blue – bit assemble into Ethernet frame. We will discuss this in details in chapter 6.
But most critical one, is here. Lookup, forwarding function. Lookup and forward is “Match plus action” behavior.
GOAL – processing at “line speed”, otherwise, buffer will be full and packet will be lost

## Slide 36: Input port functions
line
termination
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
destination-based forwarding: forward based only on destination IP address (traditional)
generalized forwarding: forward based on any set of header field values
physical layer:
bit-level reception
switch
fabric
link
layer
protocol
(receive)
link layer:
e.g., Ethernet
(chapter 6)
IMPORTANT

## Slide 37: Destination-based forwarding
Q: but what happens if ranges don’t divide up so nicely?
3
IMPORTANT
Notes: Text for this animation:
This all works out pretty nice and looks pretty simple!
But of course the devil is in the details, as the saying goes.
What happens, for example, when a subset of addresses say in this first range should go to say interface 3, rather than interface 0. Well, of course we could split the first address range into multiple pieces, and add in this new subrange with its new destination output port. But it turns out there’s a much simpler and elegant way to do this. Known as longest prefix matching.

## Slide 38: Question 4.2-2
4.2-2. Where does destination address lookup happen? Where in a router is the destination IP address looked up in a forwarding table to determine the appropriate output port to which the datagram should be directed?
(Correct) At the input port where a packet arrives.
At the output port leading to the next hop towards the destination.
Within the switching fabric.
Within the routing processor

## Slide 39: Question 4.2-3
4.2-3. Where does "match+action" happen? Where in a router does "match plus action" happen to determine the appropriate output port to which the arriving datagram should be directed?
(Correct) At the input port where a packet arrives.
At the output port leading to the next hop towards the destination.
Within the switching fabric.
Within the routing processor.

## Slide 40: Network layer: “data plane” roadmap
Network layer: overview
  data plane
  control plane
What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
Generalized Forwarding, SDN
  Match+action
  OpenFlow: match+action in action
Middleboxes

## Slide 41: Packet Scheduling: FCFS
packet scheduling: deciding which packet to send next on link
  first come, first served
  priority
  round robin
  weighted fair queueing
FCFS: packets transmitted in order of arrival to output port
also known as: First-in-first-out (FIFO)
real world examples?
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Abstraction: queue
R
IMPORTANT

## Slide 42: Scheduling policies: priority
Priority scheduling:
arriving traffic classified, queued by class
  any header fields can be used for classification
high priority queue
low priority queue
arrivals
classify
departures
link
1
3
2
4
5
arrivals
departures
packet in service
send packet from highest priority queue that has buffered packets
  FCFS within priority class
1
3
4
2
5
1
3
2
4
5
IMPORTANT

## Slide 43: Scheduling policies: round robin
Round Robin (RR) scheduling:
arriving traffic classified, queued by class
  any header fields can be used for classification
classify
arrivals
departures
link
R
server cyclically, repeatedly scans class queues, sending one complete packet from each class (if available) in turn
IMPORTANT

## Slide 44: Question 4.2-7
Packet scheduling. Consider the pattern of red and green packet arrivals to a router’s output port queue, shown below. Suppose each packet takes one time slot to be transmitted, and can only begin transmission at the beginning of a time slot after its arrival. Indicate the sequence of departing packet numbers (at t = 1, 2, 3, 4, 5, 7, 8) under FCFS, priority, round-robin scheduling.

## Slide 45: Question 4.2-7a FCFS Scheduling
1
2
3
4
5
6
7
Transmit order the same as packet arrival order of 1 2 3 4 5 6 7
1
2
3
4
5
6
7
1 2 3 4 5 6 7

## Slide 46: Question 4.2-7b Priority Scheduling
Network Layer: 4-46
1
2
3
5
4
7
6
Time 0: 1, 2 in queue, transmit 1
  FCFS within same priority
Time 1: 2, 3 in queue, transmit 2
Time 2: 3, 4 in queue, transmit 3
  FCFS within same priority
Time 3: 4, 5 in queue, transmit 5
Time 4: 4 in queue, transmit 4
Time 6: 6, 7 in queue, transmit 7
Time 7: 6 in queue, transmit 6
1 2 3 5 4 7 6
1
2
3
5
4
7
6

## Slide 47: Question 4.2-7c Round Robin Scheduling
Assume a round-robin scheduling cycle begins with red packets. i.e., (red, green) in each round.
Time 0: 1, 2 in queue, transmit 1
  1st round of (red, green)
Time 1: 2, 3 in queue, transmit 3
  1st round of (red, green)
Time 2: 2. 4 in queue, transmit 2
  2nd round of (red, green)
Time 3: 4, 5 in queue, transmit 4
  2nd round of (red, green)
Time 4: 5 in queue, transmit 5
  3RD round of (red, green). Since there is no green packet ready, this round is (red, null)
Time 6: 6, 7 in queue, transmit 7
  4th round of (red, green)
Time 7: 6 in queue, transmit 6
  4th round of (red, green)
Summary:
Times 0-1: 1st round: (1, 3)
Times 2-3: 2nd round: (2, 4)
Time 4: 3rd round: (5, null)
  No green packets ready
Times 6-7: 4th round: (7, 6)
1
3
2
4
5
7
6
1 3 2 4 5 7 6
1
3
2
4
5
7
6

## Slide 48: Network layer: “data plane” roadmap
Network layer: overview
  data plane
  control plane
What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
Generalized Forwarding, SDN
  match+action
  OpenFlow: match+action in action
Middleboxes

## Slide 49: Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
What’s a subnet ?
  device interfaces that can physically reach each other without passing through an intervening router
network consisting of 3 subnets
IP addresses have structure:
  subnet part: devices in same subnet have common high order bits
  host part: remaining low order bits
IMPORTANT

## Slide 50: Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
Recipe for defining subnets:
detach each interface from its host or router, creating “islands” of isolated networks
each isolated network is called a subnet
subnet mask: /24
(high-order 24 bits: subnet part of IP address)
subnet
223.1.3.0/24
subnet 223.1.1.0/24
subnet 223.1.2.0/24
IMPORTANT

## Slide 51: Subnets
where are the subnets?
what are the /24 subnet addresses?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
223.1.2.1
subnet 223.1.1/24
subnet 223.1.7/24
subnet 223.1.3/24
subnet 223.1.2/24
subnet 223.1.9/24
subnet 223.1.8/24
IMPORTANT

## Slide 52: IP addressing: CIDR
CIDR: Classless InterDomain Routing (pronounced “cider”)
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
IMPORTANT

## Slide 53: Question 4.3-04
4.3-04. What is a subnet? What is meant by an IP subnet? (Check zero, one or more of the following characteristics of an IP subnet).
  A A set of device interfaces that can physically reach each other without passing through an intervening router.
    Correct
  B A set of devices that always have a common first 16 bits in their IP address.
    Incorrect as the subnet mask may not be 16 bits
  C A set of devices that have a common set of leading high order bits in their IP address.
    Correct
  D A set of devices all manufactured by the same equipment maker/vendor.
    Incorrect

## Slide 54: Question 4.3-05ab
4.3-05. Subnetting(a). Consider the three subnets in the diagram below.
1. What is the maximum # of interfaces in the 223.1.2/24 network?
2. What is the maximum # of interfaces in the 223.1.3/29 network?
1 ANS: In 223.1.2/24
Network, since 32-24
=8 bits for host address,
Hence maximum # of
Interfaces = 28=256
2 ANS: In 223.1.3/29
Network, since 32-29
=3 bits for host address,
Hence maximum # of
Interfaces = 23=8
3 ANS:
subnet
part
host
part
24 bits
8 bits
29 bits
3 bits

## Slide 55: Question 4.3-05c
4.3-05. Subnetting(a). Consider the three subnets in the diagram below.
3. Which of the following addresses can not be used by an interface in the 223.1.3/29 network? Check all that apply.
  223.1.3.6, 223.1.3.2, 223.1.3.16, 223.1.2.6, 223.1.3.28
3 ANS: In 223.1.3/29
Network, since 32-29
=3 bits for host address,
Hence maximum # of
Interfaces = 23=8, ranging
From 0 to 7. Hence
223.1.3.6, 223.1.3.2 are OK
223.1.3.16, 223.1.3.28 are not OK
since the host ID exceeds 7
223.1.2.6 is not OK since network address
223.1.2 does not match 223.1.3
subnet
part
host
part
24 bits
8 bits
29 bits
3 bits

## Slide 56: Network layer: “data plane” roadmap
Network layer: overview
  data plane
  control plane
What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
Generalized Forwarding, SDN
  match+action
  OpenFlow: match+action in action
Middleboxes

## Slide 57: IP addresses: how to get one?
That’s actually two questions:
Q: How does a host get IP address within its network (host part of address)?
Q: How does a network get IP address for itself (network part of address)
How does host get IP address?
hard-coded by sysadmin in config file (e.g., /etc/rc.config in UNIX)
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”
IMPORTANT

## Slide 58: DHCP: Dynamic Host Configuration Protocol
goal: host dynamically obtains IP address from network server when it “joins” network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/on)
  support for mobile users who join/leave network
DHCP overview:
  host broadcasts DHCP discover msg [optional]
  DHCP server responds with DHCP offer msg [optional]
  host requests IP address: DHCP request msg
  DHCP server sends address: DHCP ack msg
IMPORTANT

## Slide 59: Question 4.3-06
4.3-06. Plug-and-play. What is meant by saying that DHCP is a "plug and play" protocol?
The host needs to “plug” (by wire or wirelessly) into the local network in order to access (“play” in) the Internet
No manual configuration is needed for the host to join the network., (Correct answer)
The network provides an Ethernet jack for a host’s Ethernet adapter., (Incorrect answer)

## Slide 60: IPv6: motivation
initial motivation: 32-bit IPv4 address space would be completely allocated
additional motivation:
  speed processing/forwarding: 40-byte fixed length header
  enable different network-layer treatment of “flows”
IMPORTANT

## Slide 61: IP Datagram format
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
IP protocol version number
header length(bytes)
upper layer protocol (e.g., TCP or UDP)
total datagram
length (bytes)
“type” of service:
diffserv (0:5)
ECN (6:7)
fragmentation/
reassembly
TTL: remaining max hops
(decremented at each router)
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead for TCP+IP
overhead
e.g., timestamp, record route taken
32-bit source IP address
32-bit destination IP address
header checksum
Maximum length: 64K bytes
Typically: 1500 bytes or less

## Slide 62: IPv6 datagram format
payload (data)
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
priority: identify priority among datagrams in flow
flow label: identify datagrams in same "flow.” (concept of “flow” not well defined).
128-bit
IPv6 addresses
What’s missing (compared with IPv4):
no checksum (to speed processing at routers)
no fragmentation/reassembly
no options (available as upper-layer, next-header protocol at router)
IMPORTANT

## Slide 63: Question 4.3-08
4.3-08. IPv4 versus IPv6. Which of the following fields occur ONLY in the IPv6 datagram header (i.e., appear in the IPv6 header but not in the IPv4 header)? Check all that apply.
Correct: 128-bit source and destination IP addresses.
The IP version number field.
The time-to-live (or hop limit) field.
The header checksum field.
Correct: The flow label field.
The header length field.
The options field.
The upper layer protocol (or next header) field.

## Slide 64: NAT: network address translation
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1 sends datagram to 128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router changes datagram source address from 10.0.0.1, 3345 to 138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives, destination address: 138.76.29.7, 5001
10.0.0.1
10.0.0.2
10.0.0.3
IMPORTANT

## Slide 65: Question 4.3.10
4.3.10. Network Address Translation (NAT). Which one of the following operations is not performed by NAT.?
A Generating ACKs back to the TCP sender and then taking responsibility for reliably delivery the segment to its destination, possibly using a non-TCP reliable data transfer protocol.
B On an outgoing datagram, changing the transport-layer port number of the transport-layer segment inside a datagram received from the LAN side of the NAT.
C On an incoming datagram from the public Internet side of a NAT, changing the destination IP address of a datagram to a new destination IP address that is looked up in the NAT table, and (possibly after other actions), sending that IP datagram on to the LAN side of the NAT.
D On an outgoing datagram, changing the source IP address of a datagram received from the LAN side of the NAT
ANS: A
Notes: Generating ACKs back to the TCP sender and then taking responsibility for reliably delivery the segment to its destination, possibly using a non-TCP reliable data transfer protocol.
On an outgoing datagram, changing the transport-layer port number of the transport-layer segment inside a datagram received from the LAN side of the NAT.
On an incoming datagram from the public Internet side of a NAT, changing the destination IP address of a datagram to a new destination IP address that is looked up in the NAT table, and (possibly after other actions), sending that IP datagram on to the LAN side of the NAT.
On an outgoing datagram, changing the source IP address of a datagram received from the LAN side of the NAT

## Slide 66: OpenFlow abstraction
match+action: abstraction unifies different kinds of devices
Router
  match: longest destination IP prefix
  action: forward out a link
Switch
  match: destination MAC address
  action: forward or flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port
IMPORTANT

## Slide 67: Generalized forwarding: summary
“match plus action” abstraction: match bits in arriving packet header(s) in any layers, take action
  matching over many fields (link-, network-, transport-layer)
  local actions: drop, forward, modify, or send matched packet to controller
  “program” network-wide behaviors
simple form of “network programmability”
  programmable, per-packet “processing”
  historical roots: active networking
  today: more generalized programming:
  P4 (see p4.org).
IMPORTANT

## Slide 68: Question 4.4-2
4.4-2. Generalized match+action. Which of the following match+actions can be taken in the generalized OpenFlow 1.0 match+action paradigm that we studied in Section 4.4? Check all that apply.
(Correct)... after matching on the destination IP address in the datagram header, the action taken is to forward the datagram to the output port associated with that destination IP address.
(Correct)... after matching on the destination IP address in the datagram header, the action taken is to decide whether or not to drop that datagram.
(Correct)... after matching on the port number in the segment's header, the action taken is to decide whether or not to drop that datagram containing that segment.
(Correct)... after matching on the port number in the segment's header, the action taken is to forward the datagram to the output port associated with that destination IP address.
(Correct)... after matching on the 48-bit link-layer destination MAC address, the action taken is to forward the datagram to the output port associated with that link-layer address.
(InCorrect)... after matching on the URL contained in an HTTP GET request in the TCP segment within the IP datagram, the action taken is to determine the IP address of the server associated with that URL, and to forward the datagram to the output port associated with that destination IP address.
  At the IP layer, cannot see any application layer information such as the URL contained in an HTTP GET request
(Correct)... after matching on the source and destination IP address in the datagram header, the action taken is to forward the datagram to the output port associated with that source and destination IP address pair.

## Slide 69: Flow table abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  match: pattern values in packet header fields
  actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  priority: disambiguate overlapping patterns
  counters: #bytes and #packets
Flow table
match
action
1
2
3
4
* : wildcard
src=10.1.2.3, dest=*.*.*.* send to controller
src=1.2.*.*, dest=*.*.*.* drop
src = *.*.*.*, dest=3.4.*.* forward(2)
IMPORTANT

## Slide 70: Question 4.4-4
4.4-4. Match+action in Openflow 1.0. Consider the figure below that shows the generalized forwarding table in a router. Recall that a * represents a wildcard value. Now consider an arriving datagram with the IP source and destination address fields indicated below. For each source/destination IP address pair, indicate which rule is matched. Note: assume that a rule that is earlier in the table takes priority over a rule that is later in the table and that a datagram that matches none of the table entries is dropped.

## Slide 71: Network layer: “data plane” roadmap
Network layer: overview
What’s inside a router
IP: the Internet Protocol
Generalized Forwarding
Middleboxes
  middlebox functions
  evolution, architectural principles of the Internet

## Slide 72: The IP hourglass
IP
TCP
UDP
HTTP
SMTP
QUIC
DASH
RTP
…
Ethernet
WiFi
Bluetooth
PPP
PDCP
…
copper radio fiber
Internet’s “thin waist”:
one network layer protocol: IP
must be implemented by every (billions) of Internet-connected devices
many protocols in physical, link, transport, and application layers
IMPORTANT

## Slide 73: The IP hourglass, at middle age
IP
TCP
UDP
HTTP
SMTP
QUIC
DASH
RTP
…
Ethernet
WiFi
Bluetooth
PPP
PDCP
…
copper radio fiber
Internet’s middle age “love handles”?
middleboxes, operating inside the network
NAT
NFV
Firewalls
caching
IMPORTANT

## Slide 74: Question 4.5-2
4.5-2. The "thin waist" of the Internet. What protocol (or protocols) constitutes the "thin waist" of the Internet protocol stack?
ANS: IP