## Slide 1
Chapter 1 Introduction
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Acknowledgement: Based on the textbook’s website: https://gaia.cs.umass.edu/kurose_ross/index.php
Notes: (8.2)Version
7.2 (January 2020)
All slides reformatted for 16:9 aspect ratio
Use of Calibri font, rather that Gill Sans MT
Updated slide content for 2020 link technologies and applications
Add more animation throughout
New Master slide
Feb. 2020 (8.0)
a few updates suggest by Catherine Rosenberg (thanks!)
titles in a lighter font
Sept 2020 (8.1)
Added ~7 new slides, in particular: data center slide; routing versus forwarding; security line of defense; several on encapsulation and layers (this section is a lot better now). Other relative minor changes throughout
Feb. 2023 (8.2)
few minor updates (mostly speeds, technology details)

## Slide 2: Chapter 1: roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models

## Slide 3: The network core
mesh of interconnected routers
packet-switching: hosts break application-layer messages into packets
  network forwards packets from one router to the next, across links on path from source to destination
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network

## Slide 4: Two key network-core functions
1
2
3
0111
destination address in arriving
packet’s header
routing algorithm
header value
output link
0100
0101
0111
1001
3
2
2
1
local forwarding table
Forwarding:
aka “switching”
local action: move arriving packets from router’s input link to appropriate router output link
local forwarding table
Routing:
global action: determine source-destination paths taken by packets
routing algorithms
routing algorithm

## Slide 5
routing

## Slide 6
forwarding
forwarding

## Slide 7: Packet-switching: store-and-forward
packet transmission delay: takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
source
R bps
destination
1
2
3
L bits
per packet
R bps
One-hop numerical example:
L = 10 Kbits
R = 100 Mbps
one-hop transmission delay = 0.1 msec

## Slide 8: Packet-switching: queueing
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for transmission over output link
Queueing occurs when work arrives faster than it can be serviced:

## Slide 9: Packet-switching: queueing
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for transmission over output link
Packet queuing and loss: if arrival rate (in bps) to link exceeds transmission rate (bps) of link for some period of time:
packets will queue, waiting to be transmitted on output link
packets can be dropped (lost) if memory (buffer) in router fills up

## Slide 10: Alternative to packet switching: circuit switching
end-end resources allocated to, reserved for “call” between source and destination
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive
commonly used in traditional telephone networks

## Slide 11: Circuit switching: FDM and TDM
frequency
time
frequency
time
4 users
Frequency Division Multiplexing (FDM)
optical, electromagnetic frequencies divided into (narrow) frequency bands
Time Division Multiplexing (TDM)
time divided into slots
each call allocated its own band, can transmit at max rate of that narrow band
each call allocated periodic slot(s), can transmit at maximum rate of (wider) frequency band (only) during its time slot(s)

## Slide 12: Packet switching versus circuit switching
example:
1 Gb/s link
each user:
  100 Mb/s when “active”
  active 10% of time
Q: how many users can use this network under circuit-switching and packet switching?
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive
N
users
1 Gbps link
…..
circuit-switching: 10 users
Q: how did we get value 0.0004?
A: HW problem (for those with course in probability only)
packet switching: with 35 users, probability > 10 active at same time is less than .0004 *

## Slide 13: Proof: with 35 users, probability > 10 active at same time is less than .0004
Problem Setup:
  Number of users: 35
  Probability of each user being active: 10% = 0.1
  We want to find P(X > 10), where X is the number of active users
Calculation:
  We need to calculate the probability of having 10 or fewer active users at the same time, then subtract that from 1 to get the probability of having 11 or more users active at the same time.
  First, we calculate P(X ≤ 10) using the cumulative binomial probability function:
    P(X ≤ 10) = ∑(k=0 to 10) C(35,k) * 0.1k * 0.9(35-k)
    Where C(35,k) is the binomial coefficient "35 choose k".
    Each term is probability of k users being active and (35-k) users being idle
  Then, we can find P(X > 10) by subtracting from 1:
    P(X > 10) = 1 - P(X ≤ 10) ≈ 0.0003846

## Slide 14: Packet switching versus circuit switching
great for “bursty” data – sometimes has data to send, but at other times not
  resource sharing
  simpler, no call setup
excessive congestion possible: packet delay and loss due to buffer overflow
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior with packet-switching?
  “It’s complicated.” We’ll study various techniques that try to make packet switching as “circuit-like” as possible.
Is packet switching a “slam dunk winner”?
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet switching)?

## Slide 15: Internet structure: a “network of networks”
hosts connect to Internet via access Internet Service Providers (ISPs)
access ISPs in turn must be interconnected
    so that any two hosts (anywhere!) can send packets to each other
resulting network of networks is very complex
    evolution driven by economics, national policies
Let’s take a stepwise approach to describe current Internet structure
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network

## Slide 16: Internet structure: a “network of networks”
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 17: Internet structure: a “network of networks”
…
…
…
…
…
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.

## Slide 18: Internet structure: a “network of networks”
Option: connect each access ISP to one global transit ISP?
Customer and provider ISPs have economic agreement.
global ISP
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 19: Internet structure: a “network of networks”
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….

## Slide 20: Internet structure: a “network of networks”
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors …. who will want to be connected
IXP
peering link
Internet exchange point
IXP

## Slide 21: Internet structure: a “network of networks”
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and regional networks may arise to connect access nets to ISPs
IXP
IXP
access
net
access
net
regional ISP
access
net
access
net
access
net

## Slide 22: Internet structure: a “network of networks”
ISP A
ISP C
ISP B
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and content provider networks (e.g., Google, Microsoft, Akamai) may run their own network, to bring services, content close to end users
IXP
IXP
access
net
access
net
access
net
access
net
access
net
Content provider network
regional ISP

## Slide 23: Internet structure: a “network of networks”
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
At “center”: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider networks (e.g., Google, Facebook): private network that connects its data centers to Internet, often bypassing tier-1, regional ISPs
Regional ISP
Regional ISP
Tier 1 ISP
Tier 1 ISP
IXP
Google
IXP
IXP