## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 7 Wireless and
Mobile Networks
Acknowledgement: Based on the textbook’s website: https://gaia.cs.umass.edu/kurose_ross/index.php
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
lighter header font
4G/5G material completely updated; older 2/2.5/3G removed
8.2 (July 2023). Changes from 8.0:
minor updates and additional, including removing master/slave Bluetooth language
expansion, better graphics on wireless link characteristics
expanded, significant revisions of 4G/5G material (but not mobility)

## Slide 2: Chapter 7 outline
Introduction
Wireless
Wireless links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols

## Slide 3: 4G/5G cellular networks
the solution for wide-area mobile Internet
widespread deployment/use:
  more mobile-broadband-connected devices than fixed-broadband-connected devices devices
transmission rates up to 100’s Mbps, even Gbps for 5G
technical standards: 3rd Generation Partnership Project (3GPP)
  wwww.3gpp.org
  4G: Long-Term Evolution (LTE) standard

## Slide 4: 4G/5G cellular networks
similarities to wired Internet
edge/core distinction, but both belong to same carrier
global cellular network: a network of networks
widespread use of protocols we’ve studied: HTTP, DNS, TCP, UDP, IP, NAT, separation of data/control planes, SDN, Ethernet, tunneling
interconnected to wired Internet
differences from wired Internet
different wireless link layer
mobility as a 1st class service
user “identity” (via SIM card)
business model: users subscribe to a cellular provider
  strong notion of “home network” versus roaming on visited nets
  global access, with authentication infrastructure, and inter-carrier settlements

## Slide 5: Elements of 4G LTE architecture
Mobile device
(UE)
Base station
(eNode-B)
radio access
network
all-IP Enhanced Packet Core (EPC)
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
to
Internet
…
Mobile device:
smartphone, tablet, laptop, IoT, ... with 4G LTE radio
64-bit International Mobile Subscriber Identity (IMSI), stored on SIM (Subscriber Identity Module) card
LTE jargon: User Equipment (UE)

## Slide 6: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Base station:
at “edge” of carrier’s network
manages wireless radio resources, mobile devices in its coverage area (“cell”)
coordinates device authentication with other elements
similar to WiFi AP but:
  active role in user mobility
  coordinates with nearly base stations to optimize radio use
LTE jargon: eNode-B

## Slide 7: Radio Access Network: 4G radio
connects User Equipment (UE) to a base station (eNode-B)
  multiple devices connected to each base station
many different possible frequencies bands, multiple channels in each band
  popular bands: 600, 700, 850, 1500, 1700, 1900, 2100, 2600, 3500 MHz
  separate upstream and downstream channels
sharing 4G radio channel among users:
  OFDM: Orthogonal Frequency Division Multiplexing
  combination of FDM, TDM
100’s Mbps possible per user/device
Mobile device
(UE)
Base station
(eNode-B)
Notes: G-defined subbands are narrow (e.g., 15 kHz)

## Slide 8: Spectrum
CBRS
Notes: 8 orders of magnitude: 9 Khz to 300 Ghz

## Slide 9: OFDMA: time division (LTE)
Subcarrier frequencies
time (symbols)

## Slide 10: OFDMA: time division (LTE)
time to transmit one OFDM symbol on subcarrier frequency
Physical Resource Block (PRB ): blocks of 7x12=84 resource elements
unit of transmission scheduling
Subcarrier frequencies

## Slide 11: OFDMA:
Subcarrier frequencies
time (symbols)
PRB
PRB
Transmission Time Interval (TTI): 1 ms
Transmission scheduling example:
Send to 7 UEs in 7 blocks of REs in one PRB
UE1
UE2
UE3
UE4
UE5
UE6
UE7

## Slide 12: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Home Subscriber Service
stores info about mobile devices for which the HSS’s network is their “home network”
works with MME in device authentication

## Slide 13: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Serving Gateway (S-GW), PDN Gateway (P-GW)
lie on data path from mobile to/from Internet
P-GW
  gateway to mobile cellular network
  Looks like nay other internet gateway router
  provides NAT services
other routers:
  extensive use of tunneling

## Slide 14: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Mobility Management Entity
device authentication (device-to-network, network-to-device) coordinated with mobile home network HSS
mobile device management:
  device handover between cells
  tracking/paging device location
path (tunneling) setup from mobile device to P-GW

## Slide 15: LTE: data plane control plane separation
control plane
new protocols for mobility management , security, authentication (later)
MME
HSS
base station
P-GW
S-GW
base station
P-GW
S-GW
data plane
new protocols at link, physical layers
IP tunnels
extensive use of tunneling to facilitate mobility

## Slide 16: LTE data plane protocol stack: first hop
IP
Packet Data
Convergence
Radio Link
Medium Access
Physical
data
plane
P-GW
S-GW
Application
Transport
IP
Packet Data
Convergence
Radio Link
Medium Access
Physical
Link
base station
LTE link layer protocols:
Packet Data Convergence: header compression, encryption
Radio Link Control (RLC) Protocol: fragmentation/reassembly, reliable data transfer
Medium Access: requesting, use of radio transmission slots (OFDM)

## Slide 17: LTE data plane protocol stack: packet core
IP
Packet Data
Convergence
Radio Link
Medium Access
Physical
GTP-U
UDP
IP
link
Physical
GTP-U
UDP
IP
link
Physical
GTP-U
UDP
IP
link
Physical
P-GW
S-GW
base station
\
tunneling:
mobile datagram encapsulated using GPRS Tunneling Protocol (GTP), sent inside UDP datagram to S-GW
S-GW re-tunnels datagrams to P-GW
supporting mobility: only tunneling endpoints change when mobile user moves

## Slide 18: LTE data plane: associating with a BS
data
plane
P-GW
S-GW
base station
BS broadcasts primary synch signal every 5 ms on all frequencies
BSs from multiple carriers may be broadcasting synch signals
1
mobile finds a primary synch signal, then locates 2nd synch signal on this freq.
mobile then finds info broadcast by BS: channel bandwidth, configurations; BS’s cellular carrier info
mobile may get info from multiple base stations, multiple cellular networks
2
mobile selects which BS to associate with (e.g., preference for home carrier)
3
more steps still needed to authenticate, establish state, set up data plane
4
1
2
3

## Slide 19: LTE mobiles: sleep modes
data
plane
ZZZZ...
as in WiFi, Bluetooth: LTE mobile may put radio to “sleep” to conserve battery:
light sleep: after 100’s msec of inactivity
  wake up periodically (100’s msec) to check for downstream transmissions
deep sleep: after 5-10 secs of inactivity
  mobile may change cells while deep sleeping – need to re-establish association

## Slide 20: Global cellular network: a network of IP networks
…
visited mobile
carrier network
…
public Internet
and
inter-carrier IPX
…
P-GW
P-GW
home mobile
carrier network
Home
Subscriber
Server
in home network
roaming in visited network
SIM card: global identify info in home network
all IP:
carriers interconnect with each other, and public internet at exchange points
legacy 2G, 3G: not all IP, handled otherwise
home network HSS:
identify & services info, while in home network and roaming

## Slide 21: On to 5G: motivation
From Next Generation Mobile Networks (NGMS) alliance: 2020 white paper
Hype/wishes need to be separated from reality or likely nearer-term reality

## Slide 22
“initial standards and launches have mostly focused on enhanced Mobile Broadband, 5G is expected to increasingly
enable new business models and countless new use cases, in particular those of massive Machine Type Communications and Ultra-reliable and Low Latency Communications.”
Figure: from Recommendation ITU-R M.2083-0 (2015)
On to 5G: motivation

## Slide 23
Industry verticals:
Manufacturing
Constructions
Transport
Health
Smart communities
Education
Tourism
Agriculture
Finance
K. Schwab, “The Fourth Industrial Revolution,” World Economic Forum.
eMBB
URLLC
mMTC
On to 5G: motivation

## Slide 24: On to 5G: Radio
goal: 10x increase in peak bitrate, 10x decrease in latency, 100x increase in traffic capacity over 4G
5G NR (new radio):
  two frequency bands: FR1 (450 MHz–6 GHz) and FR2 (24 GHz–52 GHz): millimeter wave frequencies
  not backwards-compatible with 4G
  MIMO: multiple directional antennae
millimeter wave frequencies: much higher data rates, but over shorter distances
  pico-cells: cells diameters: 10-100 m
  massive, dense deployment of new base stations required

## Slide 25: On to 5G: SDN-like architecture
5G: microservice-like architecture
public Internet
and
inter-carrier IPX
Mobility Management Entity (MME)
PDN gateway (P-GW)
Serving gateway (S-GW)
public Internet
and
inter-carrier IPX
Home Subscriber Service (HSS)
4G mobile core:
boxes and protocols
Notes: stream control transmission protocol (STCP)

## Slide 26: Functional elements: communication, computation, data
RAN
UE
Far Edge DC
RAN
UE
Far Edge DC
Edge DC
Mobile Core
RAN
UE
Far Edge DC
RAN
UE
Far Edge DC
Edge DC
Mobile Core
Core DC
Edge Network
Operator A
Edge Network
Operator B
Global Core
User control, Mobile Core implemented in “edge” data center (DC)

## Slide 27: Control plane: resource control
RAN
UE
Far Edge DC
RAN
UE
Far Edge DC
Edge DC
Mobile Core
RAN
UE
Far Edge DC
RAN
UE
Far Edge DC
Edge DC
Mobile Core
Core DC
Edge Network
Operator A
Edge Network
Operator B
Global Core
control plane
Real-time (< ms)
Near real-time (> ms)
Non real-time (>> ms)

## Slide 28: User plane: resources, as used by users (application)
RAN
UE
Far Edge DC
RAN
UE
Far Edge DC
Edge DC
Mobile Core
RAN
UE
Far Edge DC
RAN
UE
Far Edge DC
Edge DC
Mobile Core
Core DC
Edge Network
Operator A
Edge Network
Operator B
Global Core
User plane
“local breakout”
within one operator
edge/core
multi-operator end-end edge/core

## Slide 29: Impact of Wireless Channel on TCP
Frequent packet losses due to errors may confuse TCP as network congestion.
Wireless  High error rate  Frequent packet losses  Triggers TCP congestion control even if no overload
TCP modifications:
  Local Recovery: Link level retransmissions and error correction
  Wireless-aware TCP Sender:
  Distinguish overload (sustained) and random errors
  Split-Connection: Host1-to-AP + AP-to-Host2
Breaks layered Architecture (Upper layers are independent of lower layers)

## Slide 30: On beyond 5G?
“6G” not obviously next: “NextG” and “Beyond 5G” heard more often than “6G”
5G on an evolutionary path (like the Internet)
  agility: cloud technologies (SDN) mean new features can be introduced rapidly, deployed continuously
  customization: change can be introduced bottom-up (e.g., by enterprises and edge cloud partners with Private 5G)
    No need to wait for standardization
    No need to reach agreement (among all incumbent stakeholders)