## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 3 Transport Layer
Acknowledgement: Based on the textbook’s website: https://gaia.cs.umass.edu/kurose_ross/index.php
Notes: Version History
8.0 (April 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
added new 8th edition material on QUIC, CUBIC, delay-based congestion control
lighter header font
8.2 (July 2023): changes from 8.0
minor updates throughout, but not much changes from 8.0

## Slide 2: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 3: Principles of congestion control
Congestion:
informally: “too many sources sending too much data too fast for network to handle”
manifestations:
  long delays (queueing in router buffers)
  packet loss (buffer overflow at routers)
different from flow control!
congestion control: too many senders, sending too fast
flow control: one sender too fast for one receiver
a top-10 problem!

## Slide 4: Causes/costs of congestion: scenario 1
Simplest scenario:
maximum per-connection throughput: R/2
Host A
Host B
throughput: lout
large delays as arrival rate line approaches capacity
Q: What happens as arrival rate lin approaches R/2?
original data: lin
R
two flows
one router, infinite buffers
input, output link capacity: R
infinite shared output link buffers
R
no retransmissions needed
R/2
delay
lin
R/2
R/2
R/2
lout
lin
throughput:

## Slide 5: Causes/costs of congestion: scenario 2
one router, finite buffers
Host A
Host B
lin : original data
l'in: original data, plus retransmitted data
finite shared output link buffers
sender retransmits lost, timed-out packet
  application-layer input = application-layer output: lin = lout
  transport-layer input includes retransmissions : l’in lin
lout
R
R

## Slide 6: Causes/costs of congestion: scenario 2
Host A
Host B
lin : original data
l'in: original data, plus retransmitted data
finite shared output link buffers
copy
free buffer space!
Idealization: perfect knowledge
sender sends only when router buffers available
lout
R
R
R/2
lin
R/2
lout
throughput:

## Slide 7: Causes/costs of congestion: scenario 2
Host A
Host B
lin : original data
l'in: original data, plus retransmitted data
finite shared output link buffers
R
R
copy
no buffer space!
Idealization: some perfect knowledge
packets can be lost (dropped at router) due to full buffers
sender knows when packet has been dropped: only resends if packet known to be lost

## Slide 8: Causes/costs of congestion: scenario 2
Host A
Host B
lin : original data
l'in: original data, plus retransmitted data
finite shared output link buffers
R
R
free buffer space!
Idealization: some perfect knowledge
packets can be lost (dropped at router) due to full buffers
sender knows when packet has been dropped: only resends if packet known to be lost
when sending at R/2, some packets are needed retransmissions
lin
R/2
lout
throughput:
R/2
“wasted” capacity due to retransmissions

## Slide 9: Causes/costs of congestion: scenario 2
Host A
Host B
lin : original data
l'in: original data, plus retransmitted data
finite shared output link buffers
R
R
copy
timeout
Realistic scenario: un-needed duplicates
packets can be lost, dropped at router due to full buffers – requiring retransmissions
but sender times can time out prematurely, sending two copies, both of which are delivered
free buffer space!
when sending at R/2, some packets are retransmissions, including needed and un-needed duplicates, that are delivered!
“wasted” capacity due to un-needed retransmissions
lin
R/2
lout
throughput:
R/2

## Slide 10: Causes/costs of congestion: scenario 2
“costs” of congestion:
more work (retransmission) for given receiver throughput
unneeded retransmissions: link carries multiple copies of a packet
  decreasing maximum achievable throughput
Realistic scenario: un-needed duplicates
packets can be lost, dropped at router due to full buffers – requiring retransmissions
but sender times can time out prematurely, sending two copies, both of which are delivered
when sending at R/2, some packets are retransmissions, including needed and un-needed duplicates, that are delivered!
“wasted” capacity due to un-needed retransmissions
lin
R/2
lout
throughput:
R/2

## Slide 11: Causes/costs of congestion: scenario 3
four senders
multi-hop paths
timeout/retransmit
Q: what happens as lin and lin’ increase ?
A: as red lin’ increases, all arriving blue pkts at upper queue are dropped, blue throughput g 0
finite shared output link buffers
Host A
lout
Host B
Host C
Host D
lin : original data
l'in: original data, plus retransmitted data

## Slide 12: Causes/costs of congestion: scenario 3
another “cost” of congestion:
when packet dropped, any upstream transmission capacity and buffering used for that packet was wasted!
R/2
R/2
lout
lin’

## Slide 13: Causes/costs of congestion: insights
upstream transmission capacity / buffering wasted for packets lost downstream
delay increases as capacity approached
un-needed duplicates further decreases effective throughput
loss/retransmission decreases effective throughput
throughput can never exceed capacity

## Slide 14: Approaches towards congestion control
End-end congestion control:
no explicit feedback from network
congestion inferred from observed loss, delay
data
data
ACKs
ACKs
approach taken by TCP

## Slide 15: Approaches towards congestion control
TCP ECN, ATM, DECbit protocols
data
data
ACKs
ACKs
explicit congestion info
Network-assisted congestion control:
routers provide direct feedback to sending/receiving hosts with flows passing through congested router
may indicate congestion level or explicitly set sending rate

## Slide 16: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 17: TCP congestion control: AIMD
approach: senders can increase sending rate until packet loss (congestion) occurs, then decrease sending rate on loss event
AIMD sawtooth
behavior: probing
for bandwidth
TCP sender Sending rate
time
  increase sending rate by 1 maximum segment size every RTT until loss detected
Additive Increase
  cut sending rate in half at each loss event
Multiplicative Decrease

## Slide 18: TCP AIMD: more
Multiplicative decrease detail: sending rate is
Cut in half on loss detected by triple duplicate ACK (TCP Reno)
Cut to 1 MSS (maximum segment size) when loss detected by timeout (TCP Tahoe)
Why AIMD?
AIMD – a distributed, asynchronous algorithm – has been shown to:
  optimize congested flow rates network wide!
  have desirable stability properties

## Slide 19: TCP congestion control: details
TCP sender limits transmission:
cwnd is dynamically adjusted in response to observed network congestion (implementing TCP congestion control)
LastByteSent- LastByteAcked
<
cwnd
last byte
ACKed
last byte sent
cwnd
sender sequence number space
available but not used
TCP sending behavior:
roughly: send cwnd bytes, wait RTT for ACKS, then send more bytes
TCP rate
~
~
cwnd
RTT
bytes/sec
sent, but not-yet ACKed
(“in-flight”)

## Slide 20: TCP slow start
when connection begins, increase rate exponentially until first loss event:
  initially cwnd = 1 MSS
  double cwnd every RTT
  done by incrementing cwnd for every ACK received
Host A
one segment
Host B
RTT
time
two segments
four segments
summary: initial rate is slow, but ramps up exponentially fast

## Slide 21: TCP: from slow start to congestion avoidance
Q: when should the exponential increase switch to linear?
A: when cwnd gets to 1/2 of its value before timeout.
Implementation:
variable ssthresh
on loss event, ssthresh is set to 1/2 of cwnd just before loss event
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
X

## Slide 22: TCP CUBIC
Is there a better way than AIMD to “probe” for usable bandwidth?
Wmax
Wmax/2
classic TCP
TCP CUBIC - higher throughput in this example
Insight/intuition:
  Wmax: sending rate at which congestion loss was detected
  congestion state of bottleneck link probably (?) hasn’t changed much
  after cutting rate/window in half on loss, initially ramp to to Wmax faster, but then approach Wmax more slowly

## Slide 23: TCP CUBIC
K: point in time when TCP window size will reach Wmax
  K itself is tunable
  larger increases when further away from K
  smaller increases (cautious) when nearer K
TCP
sending
rate
time
TCP Reno
TCP CUBIC
Wmax
t0
t1
t2
t3
t4
TCP CUBIC default in Linux, most popular TCP for popular Web servers
increase W as a function of the cube of the distance between current time and K

## Slide 24: TCP and the congested “bottleneck link”
TCP (classic, CUBIC) increase TCP’s sending rate until packet loss occurs at some router’s output: the bottleneck link
source
application
TCP
network
link
physical
destination
application
TCP
network
link
physical
bottleneck link (almost always busy)
packet queue almost never empty, sometimes overflows packet (loss)

## Slide 25: TCP and the congested “bottleneck link”
TCP (classic, CUBIC) increase TCP’s sending rate until packet loss occurs at some router’s output: the bottleneck link
source
application
TCP
network
link
physical
destination
application
TCP
network
link
physical
understanding congestion: useful to focus on congested bottleneck link
insight: increasing TCP sending rate will not increase end-end throughout with congested bottleneck
insight: increasing TCP sending rate will increase measured RTT
RTT
Goal: “keep the end-end pipe just full, but not fuller”

## Slide 26: Delay-based TCP congestion control
Keeping sender-to-receiver pipe “just full enough, but no fuller”: keep bottleneck link busy transmitting, but avoid high delays/buffering
RTTmeasured
Delay-based approach:
RTTmin - minimum observed RTT (uncongested path)
uncongested throughput with congestion window cwnd is cwnd/RTTmin
if measured throughput “very close” to uncongested throughput
increase cwnd linearly /* since path not congested */
else if measured throughput “far below” uncongested throughout
decrease cwnd linearly /* since path is congested */
RTTmeasured
measured
throughput
=
# bytes sent in last RTT interval

## Slide 27: Delay-based TCP congestion control
congestion control without inducing/forcing loss
maximizing throughout (“keeping the just pipe full… ”) while keeping delay low (“…but not fuller”)
a number of deployed TCPs take a delay-based approach
  BBR deployed on Google’s (internal) backbone network

## Slide 28: Explicit congestion notification (ECN)
source
application
TCP
network
link
physical
destination
application
TCP
network
link
physical
TCP deployments often implement network-assisted congestion control:
two bits in IP header (ToS field) marked by network router to indicate congestion
  policy to determine marking chosen by network operator
congestion indication carried to destination
destination sets ECE bit on ACK segment to notify sender of congestion
involves both IP (IP header ECN bit marking) and TCP (TCP header C,E bit marking)
ECN=10
ECN=11
ECE=1
IP datagram
TCP ACK segment

## Slide 29: TCP fairness
Fairness goal: if K TCP sessions share same bottleneck link of bandwidth R, each should have average rate of R/K
TCP connection 1
bottleneck
router
capacity R
TCP connection 2

## Slide 30: Q: is TCP Fair?
Example: two competing TCP sessions:
additive increase gives slope of 1, as throughout increases
multiplicative decrease decreases throughput proportionally
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2
A: Yes, under idealized assumptions:
same RTT
fixed number of sessions only in congestion avoidance
Is TCP fair?

## Slide 31: Fairness: must all network apps be “fair”?
Fairness and UDP
multimedia apps often do not use TCP
  do not want rate throttled by congestion control
instead use UDP:
  send audio/video at constant rate, tolerate packet loss
there is no “Internet police” policing use of congestion control
Fairness, parallel TCP connections
application can open multiple parallel connections between two hosts
web browsers do this , e.g., link of rate R with 9 existing connections:
  new app asks for 1 TCP, gets rate R/10
  new app asks for 11 TCPs, gets R/2