## Slide 2: Dijkstra's Algorithm vs. Bellman-Ford Algorithm
Dijkstra's Algorithm:
  Uses a priority queue to select the next vertex to process.
  Greedily selects the vertex with the smallest tentative distance to source node.
  Works only on graphs with non-negative edge weights.
Bellman-Ford Algorithm:
  Iteratively relaxes all edges V-1 times, where V is the number of vertices.
  Does not use a priority queue.
  Can handle graphs with negative edge weights, and can detect negative cycles.
Dijkstra's algorithm is faster and more efficient for graphs with non-negative weights, the Bellman-Ford algorithm is more versatile as it can handle negative weights and detect negative cycles, albeit at the cost of lower efficiency.
Notes: Dijkstra's Algorithm:
- Finds the shortest path from a single source vertex to all other vertices in a graph with non-negative edge weights.
**Bellman-Ford Algorithm:**
- Finds the shortest path from a single source vertex to all other vertices in a graph, even with negative edge weights.
- Can detect negative cycles in the graph.
## Edge Weight Handling
**Dijkstra's Algorithm:**
- Works only on graphs with non-negative edge weights.
**Bellman-Ford Algorithm:**
- Can handle graphs with negative edge weights.
- Can detect negative cycles.
## Performance
Dijkstra's Algorithm:
- More efficient for graphs with non-negative weights.
- Time complexity: O(V log V + E) with a binary heap implementation, where V is the number of vertices and E is the number of edges.
**Bellman-Ford Algorithm:**
- Generally slower than Dijkstra's.
- Time complexity: O(VE), where V is the number of vertices and E is the number of edges.
## Implementation

## Slide 3: The DV Algorithm
A router transmits its distance vector to each of its neighbors in a routing packet.
Each router receives and saves the most recently received distance vector from each of its neighbors.
A router recalculates its distance vector when:
  It receives a distance vector from a neighbor containing different information than before.
  It discovers that a link to a neighbor has gone down.
The DV calculation is based on minimizing the cost to each destination
Dx(y) = Estimate of least cost from x to y
C(x,v) = Node x knows cost to each neighbor v
Dx = [Dx(y): y ? N ] = Node x maintains distance vector
Node x also maintains its neighbors' distance vectors
– For each neighbor v, x maintains Dv = [Dv(y): y ? N ]

## Slide 4
From time-to-time, each node sends its own distance vector estimate to neighbors.
When a node x receives new DV estimate from any neighbor v, it saves v’s distance vector and it updates its own DV using B-F equation:

## Slide 5: Network layer: “data plane” roadmap
Network layer: overview
  data plane
  control plane
What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
Generalized Forwarding, SDN
  match+action
  OpenFlow: match+action in action
Middleboxes

## Slide 6: IP addresses: how to get one?
That’s actually two questions:
Q: How does a host get IP address within its network (host part of address)?
Q: How does a network get IP address for itself (network part of address)
How does host get IP address?
hard-coded by sysadmin in config file (e.g., /etc/rc.config in UNIX)
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”
IMPORTANT

## Slide 7: DHCP: Dynamic Host Configuration Protocol
goal: host dynamically obtains IP address from network server when it “joins” network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/on)
  support for mobile users who join/leave network
DHCP overview:
  host broadcasts DHCP discover msg [optional]
  DHCP server responds with DHCP offer msg [optional]
  host requests IP address: DHCP request msg
  DHCP server sends address: DHCP ack msg
IMPORTANT

## Slide 8: Question 4.3-06
4.3-06. Plug-and-play. What is meant by saying that DHCP is a "plug and play" protocol?
The host needs to “plug” (by wire or wirelessly) into the local network in order to access (“play” in) the Internet
No manual configuration is needed for the host to join the network., (Correct answer)
The network provides an Ethernet jack for a host’s Ethernet adapter., (Incorrect answer)

## Slide 9: Network layer: “data plane” roadmap
Network layer: overview
What’s inside a router
IP: the Internet Protocol
Generalized Forwarding
Middleboxes
  middlebox functions
  evolution, architectural principles of the Internet

## Slide 10: The IP hourglass
IP
TCP
UDP
HTTP
SMTP
QUIC
DASH
RTP
…
Ethernet
WiFi
Bluetooth
PPP
PDCP
…
copper radio fiber
Internet’s “thin waist”:
one network layer protocol: IP
must be implemented by every (billions) of Internet-connected devices
many protocols in physical, link, transport, and application layers
IMPORTANT

## Slide 11: The IP hourglass, at middle age
IP
TCP
UDP
HTTP
SMTP
QUIC
DASH
RTP
…
Ethernet
WiFi
Bluetooth
PPP
PDCP
…
copper radio fiber
Internet’s middle age “love handles”?
middleboxes, operating inside the network
NAT
NFV
Firewalls
caching
IMPORTANT

## Slide 12: Question 4.5-2
4.5-2. The "thin waist" of the Internet. What protocol (or protocols) constitutes the "thin waist" of the Internet protocol stack?