## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 7 Wireless and
Mobile Networks
Acknowledgement: Based on the textbook’s website: https://gaia.cs.umass.edu/kurose_ross/index.php
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
lighter header font
4G/5G material completely updated; older 2/2.5/3G removed
8.2 (July 2023). Changes from 8.0:
minor updates and additional, including removing master/slave Bluetooth language
expansion, better graphics on wireless link characteristics
expanded, significant revisions of 4G/5G material (but not mobility)

## Slide 2: Wireless and Mobile Networks: context
more wireless (mobile) phone subscribers than fixed (wired) phone subscribers (10-to-1 in 2019)!
more mobile-broadband-connected devices than fixed-broadband-connected devices devices (5-1 in 2019)!
  4G/5G cellular networks now embracing Internet protocol stack, including SDN
two important (but different) challenges
  wireless: communication over wireless link
  mobility: handling the mobile user who changes point of attachment to network

## Slide 3: Chapter 7 outline
Introduction
Wireless
Wireless Links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols

## Slide 4: Elements of a wireless network
wired network
infrastructure

## Slide 5: Elements of a wireless network
wired network
infrastructure
wireless hosts
laptop, smartphone, IoT
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility!

## Slide 6: Elements of a wireless network
wired network
infrastructure
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points

## Slide 7: Elements of a wireless network
wired network
infrastructure
wireless link
typically used to connect mobile(s) to base station, also used as backbone link
multiple access protocol coordinates link access
various transmission rates and distances, frequency bands

## Slide 8: Characteristics of selected wireless links
Indoor
Outdoor
Midrange
outdoor
Long range
outdoor
10-30m
50-200m
200m-4Km
4Km-15Km
2 Mbps
4G LTE
802.11ac
802.11n
802.11g
802.11b
3.5 Gbps
600 Mbps
54 Mbps
11 Mbps
Bluetooth
802.11ax
14 Gbps
5G
10 Gbps
802.11 af,ah

## Slide 9: Elements of a wireless network
wired network
infrastructure
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network

## Slide 10: Elements of a wireless network
ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: route among themselves

## Slide 11: Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to base station (WiFi, cellular) which connects to larger Internet
no base station, no connection to larger Internet (Bluetooth, ad hoc nets)
host may have to relay through several wireless nodes to connect to larger
Internet: mesh net
no base station, no connection to larger Internet. May have to relay to reach other a given wireless node MANET, VANET

## Slide 12: Chapter 7 outline
Introduction
Wireless
Wireless links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols

## Slide 13: Wireless link characteristics: fading (attenuation)
  Wireless radio signal attenuates (loses power) as it propagates (free space “path loss”)
Free space path loss ~ (fd)2
f: frequency
d: distance
higher frequency or longer distance
larger free space
path loss
Notes: Wikipedia figure

## Slide 14: Wireless link characteristics: multipath
  multipath propagation: radio signal reflects off objects ground, built environment, arriving at destination at slightly different times
line of sight
(LOS) path
reflected path
reflected path

## Slide 15: Wireless link characteristics: multipath
  multipath propagation: radio signal reflects off objects ground, built environment, arriving at destination at slightly different times
Tc: coherence time
Coherence time:
amount of time bit is present in channel to be received
influences maximum possible transmission rate, since coherence times can not overlap
inversely proportional to
  frequency
  receiver velocity
transmitted
pulses
received
pulse
received
LOS pulse
received
multipath
pulses
time
time
received
LOS pulse
received
multipath
pulses

## Slide 16: Wireless link characteristics: noise
interference from other sources on wireless network frequencies: motors, appliances
SNR: signal-to-noise ratio
  larger SNR – easier to extract signal from noise (a “good thing”)
SNR versus BER tradeoff
  given physical layer: increase power -> increase SNR->decrease BER
  SNR may change with mobility: dynamically adapt physical layer (modulation technique, rate)
10
20
30
40
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4

## Slide 17: Wireless link characteristics: hidden terminals
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Attenuation also causes “hidden terminals”
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B

## Slide 18: Chapter 7 outline
Introduction
Wireless
Wireless links and network characteristics
CDMA: code division multiple access
WiFi: 802.11 wireless LANs
Bluetooth

## Slide 19: Code Division Multiple Access (CDMA)
unique “code” assigned to each user; i.e., code set partitioning
  all users share same frequency, but each user has own chipping sequence (i.e., code) to encode data
  allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”)
  analogy: people speaking different languages in the same roo do not interfere with each other
encoding: scalar-vector product: (original data) (chipping sequence)
  d (x1, x2, … , xn) = (d*x1, d*x2, …, d*xn), where d = 1 or -1.
decoding: vector-vector inner-product: (encoded data) (chipping sequence)
  Defined as sum of elementwise product:
  (x1, x2, … , xn) (y1, y2, … , yn) = (x1*y1+x2*y2+…+xn*yn)

## Slide 20: Direct-Sequence Spread Spectrum CDMA
Chipping sequence (Code): (1,1,1,-1,1,-1,-1,-1)
The 8-bit sequence 1*(1,1,1,-1,1,-1,-1,-1) encodes data bit 1 (corresponding to application bit 1).
The 8-bit sequence (-1)*(1,1,1,-1,1,-1,-1,-1) = (-1,-1,-1,1,-1,1,1,1) encodes data bit -1 (corresponding to application bit 0).
Spreading factor = Code length/data bit = 8
  10-100 commercial (Min 10 by FCC), 10,000 for military
1
1
1
1
-1
-1
-1
Notes: Signal bandwidth > 10 × data bandwidth
Code sequence synchronization
Zi,m= di.cm
-1*(1,1,1,-1,1,-1,-1,-1) = (-1,-1,-1,1,-1,1,1,1)
1*(1,1,1,-1,1,-1,-1,-1) = (1,1,1,-1,1,-1,-1,-1)
Correlation between codes  Interference  Orthogonal

## Slide 21: CDMA encode/decode
slot 1
slot 0
d1 = -1
1
1
1
1
1
-
1
-
1
-
1
-
Zi,m= di.cm
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
channel output Zi,m
sender
code
data
bits
slot 1
slot 0
d1 = -1
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
receiver
code
received
input
di = S Zi,m.cm
m=1
M
M
Encoded data in slot 1:
-1*(1,1,1,-1,1,-1,-1,-1)
= (-1,-1,-1,1,-1,1,1,1)
Decoded data in slot 1:
= (1/8)*(-1,-1,-1,1,-1,1,1,1) ⋅ (1,1,1,-1,1,-1,-1,-1)
= -1

## Slide 22: CDMA encode/decode
Sender 1 Code : (1,1,1,-1,1,-1,-1,-1)
Encoded data in slot 1:
  -1*(1,1,1,-1,1,-1,-1,-1)
  = (-1,-1,-1,1,-1,1,1,1)
Decoded data in slot 1 is normalized (divided by code length ) inner product of the encoded with Sender 1 Code:
  = (1/8)*(-1,-1,-1,1,-1,1,1,1) (1,1,1,-1,1,-1,-1,-1)
  = (1/8)*((-1)*1+(-1)*1+(-1)*1+1*(-1) +(-1)*1+1*(-1)+1*(-1)+1*(-1))
  = (1/8)*(-8)
  = -1

## Slide 23: CDMA: two-sender interference
using same code as sender 1, receiver recovers sender 1’s original data from summed channel data!
Sender 1
Sender 2
channel sums together transmissions by sender 1 and 2
provided the codes for different
senders are orthogonal
M=8 (# bits)
Encoded data in slot 1:
-1*(1,1,1,-1,1,-1,-1,-1)
+ 1*(1,-1,1,1,1,-1,1,1)
= (0,-2,0,2,0,0,2,2)
Decoded data in slot 1 for Sender 1:
=(1/8)*(0*1+(-2)*1+0*1+2*(-1)
+0*1+0*(-1)+2*(-1)+2*(-1))
=(1/8)*(-8)=-1

## Slide 24: CDMA: two-sender interference
Orthogonal codes:
  Sender 1 Code: : (1,1,1,-1,1,-1,-1,-1)
  Sender 2 Code: (1,-1,1,1,1,-1,1,1)
  Orthogonal since their inner product is 0:
  (1,1,1,-1,1,-1,-1,-1) (1,-1,1,1,1,-1,1,1)
  =1*1+1*(-1)+1*1+(-1)*1 +1*1+(-1)*(-1)+(-1)*1+(-1)*1
  =0
Encoded data in slot 1 is sum of encoded -1 for Sender 1 and encoded 1 for Sender 2:
  -1*(1,1,1,-1,1,-1,-1,-1) + 1*(1,-1,1,1,1,-1,1,1)
  = (0,-2,0,2,0,0,2,2)
Decoded data for Sender 1 in slot 1 is :
  = (1/8)*(0,-2,0,2,0,0,2,2) (1,1,1,-1,1,-1,-1,-1)
  =(1/8)*(0*1+(-2)*1+0*1+2*(-1) +0*1+0*(-1)+2*(-1)+2*(-1))
  =(1/8)*(-8)
  =-1
Decoded data for Sender 2 in slot 1 is :
  = (1/8)*(0,-2,0,2,0,0,2,2) (1,-1,1,1,1,-1,1,1)
  =(1/8)*(0*1+(-2)*(-1)+0*1+2*1+0*1+0*(-1)+2*1+2*1)
  =(1/8)*8
  =1

## Slide 25: CDMA: two-sender interference: Explanations
Decoded data for Sender 1 in slot 1 is
=(1/8)*((-1)*(1,1,1,-1,1,-1,-1,-1) + 1*(1,-1,1,1,1,-1,1,1)) (1,1,1,-1,1,-1,-1,-1))
=(1/8)*((-1)*(1,1,1,-1,1,-1,-1,-1) (1,1,1,-1,1,-1,-1,-1) + (1/8)*1*(1,-1,1,1,1,-1,1,1) (1,1,1,-1,1,-1,-1,-1))
(First term: Sender 1 Code’s inner product with itself with itself is sum of M 1’s, M=8 is its dimension. Second term: Sender 1 Code’s inner product with Sender 2 Code equals 0, since the codes for different senders are orthogonal)
= (1/8)*(-1*(1+1+1+1+1+1+1+1) + 1*(1*1+1*(-1)+1*1+(-1)*1 +1*1+(-1)*(-1)+(-1)*1+(-1)*1))
= (1/8)*(-1*8 + 1*0)
= -1

## Slide 26: Quiz 1
Q1: Consider the codes for two senders: Sender 1 Code: (1,-1,-1,-1,1,-1,-1,-1), Sender 2 Code: (1,-1,1,-1,1,-1,1,-1). Are they orthogonal?
Q2: Consider the codes for two senders: Sender 1 Code: (1,-1,1,-1,1,-1,-1,-1), Sender 2 Code: (1,1,1,1,1,-1,1,-1). Are they orthogonal?
Q3: With the codes in Q2, suppose Sender 1 sends data bit 1 and Sender 2 sends data bit -1 simultaneously, compute the encoded data.
Q4: Compute the decoded data bit for Sender 1 and decoded data bit Sender 2.

## Slide 27: Quiz 2
Q: A CDMA receiver receives the following encoded data:
(-1 +1 -3 +1 -1 -3 +1 +1).
Assuming the following codes used by four sending stations (they are pairwise orthogonal to each other),
  A=(-1,-1,-1,+1,+1,-1,+1,+1)
  B=(-1,-1,+1,-1,+1,+1,+1,-1)
  C=(-1,+1,-1,+1,+1,+1,-1,-1)
  D=(-1,+1,-1,-1,-1,-1,+1,-1)
which stations transmitted, and which bits did each one send?
A: Compute the normalized inner products with each code:
  A’s data:(1/8)*(-1 +1 -3 +1 -1 -3 +1 +1) (-1,-1,-1,+1,+1,-1,+1,+1)/8 = 1
  B’s data:(1/8)*(-1 +1 -3 +1 -1 -3 +1 +1) (-1-1+1-1+1+1+1-1)/8=-1
  C’s data:(1/8)*(-1 +1 -3 +1 -1 -3 +1 +1) (-1+1-1+1+1+1-1-1)/8=0
  D’s data:(1/8)* (-1 +1 -3 +1 -1 -3 +1 +1) (-1-1-1-1-1-1-1-1)/8 = 1
Clearly, stations A, B, and D transmitted bits 1, -1, 1 respectively while station C did not transmit.
  Corresponding to application bits 1, 0, 1