## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 7 Wireless and
Mobile Networks
Acknowledgement: Based on the textbook’s website: https://gaia.cs.umass.edu/kurose_ross/index.php
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
lighter header font
4G/5G material completely updated; older 2/2.5/3G removed
8.2 (July 2023). Changes from 8.0:
minor updates and additional, including removing master/slave Bluetooth language
expansion, better graphics on wireless link characteristics
expanded, significant revisions of 4G/5G material (but not mobility)

## Slide 2: Wireless and Mobile Networks: context
more wireless (mobile) phone subscribers than fixed (wired) phone subscribers (10-to-1 in 2019)!
more mobile-broadband-connected devices than fixed-broadband-connected devices devices (5-1 in 2019)!
  4G/5G cellular networks now embracing Internet protocol stack, including SDN
two important (but different) challenges
  wireless: communication over wireless link
  mobility: handling the mobile user who changes point of attachment to network

## Slide 3: Chapter 7 outline
Introduction
Wireless
Wireless Links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols

## Slide 4: Elements of a wireless network
wired network
infrastructure

## Slide 5: Elements of a wireless network
wired network
infrastructure
wireless hosts
laptop, smartphone, IoT
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility!

## Slide 6: Elements of a wireless network
wired network
infrastructure
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points

## Slide 7: Elements of a wireless network
wired network
infrastructure
wireless link
typically used to connect mobile(s) to base station, also used as backbone link
multiple access protocol coordinates link access
various transmission rates and distances, frequency bands

## Slide 8: Characteristics of selected wireless links
Indoor
Outdoor
Midrange
outdoor
Long range
outdoor
10-30m
50-200m
200m-4Km
4Km-15Km
2 Mbps
4G LTE
802.11ac
802.11n
802.11g
802.11b
3.5 Gbps
600 Mbps
54 Mbps
11 Mbps
Bluetooth
802.11ax
14 Gbps
5G
10 Gbps
802.11 af,ah

## Slide 9: Elements of a wireless network
wired network
infrastructure
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network

## Slide 10: Elements of a wireless network
ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: route among themselves

## Slide 11: Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to base station (WiFi, cellular) which connects to larger Internet
no base station, no connection to larger Internet (Bluetooth, ad hoc nets)
host may have to relay through several wireless nodes to connect to larger
Internet: mesh net
no base station, no connection to larger Internet. May have to relay to reach other a given wireless node MANET, VANET

## Slide 12: Chapter 7 outline
Introduction
Wireless
Wireless links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols

## Slide 13: Wireless link characteristics: fading (attenuation)
  Wireless radio signal attenuates (loses power) as it propagates (free space “path loss”)
Free space path loss ~ (fd)2
f: frequency
d: distance
higher frequency or longer distance
larger free space
path loss
Notes: Wikipedia figure

## Slide 14: Wireless link characteristics: multipath
  multipath propagation: radio signal reflects off objects ground, built environment, arriving at destination at slightly different times
line of sight
(LOS) path
reflected path
reflected path

## Slide 15: Wireless link characteristics: multipath
  multipath propagation: radio signal reflects off objects ground, built environment, arriving at destination at slightly different times
Tc: coherence time
Coherence time:
amount of time bit is present in channel to be received
influences maximum possible transmission rate, since coherence times can not overlap
inversely proportional to
  frequency
  receiver velocity
transmitted
pulses
received
pulse
received
LOS pulse
received
multipath
pulses
time
time
received
LOS pulse
received
multipath
pulses

## Slide 16: Wireless link characteristics: noise
interference from other sources on wireless network frequencies: motors, appliances
SNR: signal-to-noise ratio
  larger SNR – easier to extract signal from noise (a “good thing”)
SNR versus BER tradeoff
  given physical layer: increase power -> increase SNR->decrease BER
  SNR may change with mobility: dynamically adapt physical layer (modulation technique, rate)
10
20
30
40
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4

## Slide 17: Wireless link characteristics: hidden terminals
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Attenuation also causes “hidden terminals”
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B

## Slide 18: Chapter 7 outline
Introduction
Wireless
Wireless links and network characteristics
CDMA: code division multiple access
WiFi: 802.11 wireless LANs
Bluetooth

## Slide 19: Code Division Multiple Access (CDMA)
unique “code” assigned to each user; i.e., code set partitioning
  all users share same frequency, but each user has own chipping sequence (i.e., code) to encode data
  allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”)
  analogy: people speaking different languages in the same roo do not interfere with each other
encoding: scalar-vector product: (original data) (chipping sequence)
  d (x1, x2, … , xn) = (d*x1, d*x2, …, d*xn), where d = 1 or -1.
decoding: vector-vector inner-product: (encoded data) (chipping sequence)
  Defined as sum of elementwise product:
  (x1, x2, … , xn) (y1, y2, … , yn) = (x1*y1+x2*y2+…+xn*yn)

## Slide 20: Direct-Sequence Spread Spectrum CDMA
Chipping sequence (Code): (1,1,1,-1,1,-1,-1,-1)
The 8-bit sequence 1*(1,1,1,-1,1,-1,-1,-1) encodes data bit 1 (corresponding to application bit 1).
The 8-bit sequence (-1)*(1,1,1,-1,1,-1,-1,-1) = (-1,-1,-1,1,-1,1,1,1) encodes data bit -1 (corresponding to application bit 0).
Spreading factor = Code length/data bit = 8
  10-100 commercial (Min 10 by FCC), 10,000 for military
1
1
1
1
-1
-1
-1
Notes: Signal bandwidth > 10 × data bandwidth
Code sequence synchronization
Zi,m= di.cm
-1*(1,1,1,-1,1,-1,-1,-1) = (-1,-1,-1,1,-1,1,1,1)
1*(1,1,1,-1,1,-1,-1,-1) = (1,1,1,-1,1,-1,-1,-1)
Correlation between codes  Interference  Orthogonal

## Slide 21: CDMA encode/decode
slot 1
slot 0
d1 = -1
1
1
1
1
1
-
1
-
1
-
1
-
Zi,m= di.cm
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
channel output Zi,m
sender
code
data
bits
slot 1
slot 0
d1 = -1
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
receiver
code
received
input
di = S Zi,m.cm
m=1
M
M
Encoded data in slot 1:
-1*(1,1,1,-1,1,-1,-1,-1)
= (-1,-1,-1,1,-1,1,1,1)
Decoded data in slot 1:
= (1/8)*(-1,-1,-1,1,-1,1,1,1) ⋅ (1,1,1,-1,1,-1,-1,-1)
= -1

## Slide 22: CDMA encode/decode
Sender 1 Code : (1,1,1,-1,1,-1,-1,-1)
Encoded data in slot 1:
  -1*(1,1,1,-1,1,-1,-1,-1)
  = (-1,-1,-1,1,-1,1,1,1)
Decoded data in slot 1 is normalized (divided by code length ) inner product of the encoded with Sender 1 Code:
  = (1/8)*(-1,-1,-1,1,-1,1,1,1) (1,1,1,-1,1,-1,-1,-1)
  = (1/8)*((-1)*1+(-1)*1+(-1)*1+1*(-1) +(-1)*1+1*(-1)+1*(-1)+1*(-1))
  = (1/8)*(-8)
  = -1

## Slide 23: CDMA: two-sender interference
using same code as sender 1, receiver recovers sender 1’s original data from summed channel data!
Sender 1
Sender 2
channel sums together transmissions by sender 1 and 2
provided the codes for different
senders are orthogonal
M=8 (# bits)
Encoded data in slot 1:
-1*(1,1,1,-1,1,-1,-1,-1)
+ 1*(1,-1,1,1,1,-1,1,1)
= (0,-2,0,2,0,0,2,2)
Decoded data in slot 1 for Sender 1:
=(1/8)*(0*1+(-2)*1+0*1+2*(-1)
+0*1+0*(-1)+2*(-1)+2*(-1))
=(1/8)*(-8)=-1

## Slide 24: CDMA: two-sender interference
Orthogonal codes:
  Sender 1 Code: : (1,1,1,-1,1,-1,-1,-1)
  Sender 2 Code: (1,-1,1,1,1,-1,1,1)
  Orthogonal since their inner product is 0:
  (1,1,1,-1,1,-1,-1,-1) (1,-1,1,1,1,-1,1,1)
  =1*1+1*(-1)+1*1+(-1)*1 +1*1+(-1)*(-1)+(-1)*1+(-1)*1
  =0
Encoded data in slot 1 is sum of encoded -1 for Sender 1 and encoded 1 for Sender 2:
  -1*(1,1,1,-1,1,-1,-1,-1) + 1*(1,-1,1,1,1,-1,1,1)
  = (0,-2,0,2,0,0,2,2)
Decoded data for Sender 1 in slot 1 is :
  = (1/8)*(0,-2,0,2,0,0,2,2) (1,1,1,-1,1,-1,-1,-1)
  =(1/8)*(0*1+(-2)*1+0*1+2*(-1) +0*1+0*(-1)+2*(-1)+2*(-1))
  =(1/8)*(-8)
  =-1
Decoded data for Sender 2 in slot 1 is :
  = (1/8)*(0,-2,0,2,0,0,2,2) (1,-1,1,1,1,-1,1,1)
  =(1/8)*(0*1+(-2)*(-1)+0*1+2*1+0*1+0*(-1)+2*1+2*1)
  =(1/8)*8
  =1

## Slide 25: CDMA: two-sender interference: Explanations
Decoded data for Sender 1 in slot 1 is
=(1/8)*((-1)*(1,1,1,-1,1,-1,-1,-1) + 1*(1,-1,1,1,1,-1,1,1)) (1,1,1,-1,1,-1,-1,-1))
=(1/8)*((-1)*(1,1,1,-1,1,-1,-1,-1) (1,1,1,-1,1,-1,-1,-1) + (1/8)*1*(1,-1,1,1,1,-1,1,1) (1,1,1,-1,1,-1,-1,-1))
(First term: Sender 1 Code’s inner product with itself with itself is sum of M 1’s, M=8 is its dimension. Second term: Sender 1 Code’s inner product with Sender 2 Code equals 0, since the codes for different senders are orthogonal)
= (1/8)*(-1*(1+1+1+1+1+1+1+1) + 1*(1*1+1*(-1)+1*1+(-1)*1 +1*1+(-1)*(-1)+(-1)*1+(-1)*1))
= (1/8)*(-1*8 + 1*0)
= -1

## Slide 26: Quiz 1
Q1: Consider the codes for two senders: Sender 1 Code: (1,-1,-1,-1,1,-1,-1,-1), Sender 2 Code: (1,-1,1,-1,1,-1,1,-1). Are they orthogonal?
Q2: Consider the codes for two senders: Sender 1 Code: (1,-1,1,-1,1,-1,-1,-1), Sender 2 Code: (1,1,1,1,1,-1,1,-1). Are they orthogonal?
Q3: With the codes in Q2, suppose Sender 1 sends data bit 1 and Sender 2 sends data bit -1 simultaneously, compute the encoded data.
Q4: Compute the decoded data bit for Sender 1 and decoded data bit Sender 2.

## Slide 27: Quiz 2
Q: A CDMA receiver receives the following encoded data:
(-1 +1 -3 +1 -1 -3 +1 +1).
Assuming the following codes used by four sending stations (they are pairwise orthogonal to each other),
  A=(-1,-1,-1,+1,+1,-1,+1,+1)
  B=(-1,-1,+1,-1,+1,+1,+1,-1)
  C=(-1,+1,-1,+1,+1,+1,-1,-1)
  D=(-1,+1,-1,-1,-1,-1,+1,-1)
which stations transmitted, and which bits did each one send?
A: Compute the normalized inner products with each code:
  A’s data:(1/8)*(-1 +1 -3 +1 -1 -3 +1 +1) (-1,-1,-1,+1,+1,-1,+1,+1)/8 = 1
  B’s data:(1/8)*(-1 +1 -3 +1 -1 -3 +1 +1) (-1-1+1-1+1+1+1-1)/8=-1
  C’s data:(1/8)*(-1 +1 -3 +1 -1 -3 +1 +1) (-1+1-1+1+1+1-1-1)/8=0
  D’s data:(1/8)* (-1 +1 -3 +1 -1 -3 +1 +1) (-1-1-1-1-1-1-1-1)/8 = 1
Clearly, stations A, B, and D transmitted bits 1, -1, 1 respectively while station C did not transmit.
  Corresponding to application bits 1, 0, 1

## Slide 28: Chapter 7 outline
Introduction
Wireless
Wireless links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols

## Slide 29: IEEE 802.11 Wireless LAN
IEEE 802.11 standard | Year | Max data rate | Range | Frequency
802.11b | 1999 | 11 Mbps | 30 m | 2.4 Ghz
802.11g | 2003 | 54 Mbps | 30m | 2.4 Ghz
802.11n (WiFi 4) | 2009 | 600 | 70m | 2.4, 5 Ghz
802.11ac (WiFi 5) | 2013 | 3.47Gpbs | 70m | 5 Ghz
802.11ax (WiFi 6) | 2020 (exp.) | 14 Gbps | 70m | 2.4, 5 Ghz
802.11af | 2014 | 35 – 560 Mbps | 1 Km | unused TV bands (54-790 MHz)
802.11ah | 2017 | 347Mbps | 1 Km | 900 Mhz
all use CSMA/CA for multiple access, and differ in the physical layer (frequency range)
For the same power and coding, higher frequency (longer wavelengths) will have lower data rate and longer distances.

## Slide 30: Wireless Network Taxonomy
(
 | Single hop | Multiple hops
Infrastructure Access Points, Towers) | Host connects to base station (WiFi, WiMAX, cellular) which connects to larger Internet | Host may have to relay through several wireless nodes to connect to larger Internet: Mesh net
No Infrastructure | No base station (Bluetooth, ad hoc nets) | Relay to reach other a given wireless node. Mobile Ad- hoc Network (MANET), Vehicular Ad-hoc Network (VANET)

## Slide 31: Hidden Node Problem
B and A can hear each other B and C can hear each other
A and C cannot hear each other
 C is hidden for A and vice versa
C may start transmitting while A is also transmitting A and C can't detect collision.
Only the receiver can help avoid collisions
A
B
C
A
B
C

## Slide 32: 802.11 LAN architecture
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
switch
or router

## Slide 33: 802.11: Channels
spectrum divided into channels at different frequencies
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
Example: 2.4 GHz
Notes: recall that 802.11 operates in the frequency range of 2.4 GHz to 2.4835 GHz. Within this 85 MHz band, 802.11 defines 11 partially overlapping channels.

## Slide 34: 802.11: Association
arriving host: must associate with an AP
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with
  then may perform authentication [Chapter 8]
  then typically run DHCP to get IP address in AP’s subnet
BSS

## Slide 35: 802.11: passive/active scanning
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
3
1
passive scanning:
beacon frames sent from APs
association Request frame sent: H1 to selected AP
association Response frame sent from selected AP to H1
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
2
3
4
active scanning:
Probe Request frame broadcast from H1
Probe Response frames sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent from selected AP to H1

## Slide 36: IEEE 802.11: multiple access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with detected ongoing transmission by another node
802.11: no collision detection!
  difficult to sense collisions: high transmitting signal, weak received signal due to fading
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/CollisionAvoidance
space
A
B
C
A
B
C
A’s signal
strength
C’s signal
strength

## Slide 37: 4-Way Handshake
Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA)
Listen before you talk. If the medium is busy, the transmitter backs off for a random period.
Avoids collision by sending a short message: Ready to send (RTS)
RTS contains dest. address and duration of message. Tells everyone to backoff for the duration.
Destination sends: Clear to send (CTS)
Can not detect collision  Each packet is acked.
MAC level retransmission if not acked.
Access Point
Mobile Node
Ready to send (RTS)
Data
Clear to send (CTS)
Ack

## Slide 38: IEEE 802.11 Architecture
Station Station
Station
Station
Ad-hoc Station
Ad-hoc Station
Access Point
Access Point
Basic Service Set
2nd BSS
Server
Ad-hoc network

## Slide 39: IEEE 802.11 Architecture Cont
Basic Service Area (BSA) = Cell
  Area: Geographical area = a room, or a building
Each BSA may have several wireless LANs
Extended Service Area (ESA) = Multiple BSAs interconnected via Access Points (AP) = Multiple rooms in your home with different extenders advertising the same SSID
Basic Service Set (BSS)
  = Set of stations associated with an AP ={MAC1,…,MACn}. Each BSS has a Service Set ID (SSID), e. g., WUSTL-Guest
Extended Service Set (ESS)
  = Set of stations in an ESA
Ad-hoc networks coexist and interoperate with infrastructure- based networks.

## Slide 40: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS (Distributed Interframe Space) then
  transmit entire frame (no CD)
sender
receiver
DIFS
data
SIFS
ACK
802.11 receiver
if frame received OK
return ACK after SIFS (Short Interframe Space) (ACK needed due to hidden terminal problem)
SIFS is a shorter interframe space used between frames of an ongoing communication session where no contention is required.
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2

## Slide 41: Avoiding collisions (more)
idea: sender “reserves” channel use for data frames using small reservation packets
sender first transmits small request-to-send (RTS) packet to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
CTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions

## Slide 42: Collision Avoidance: RTS-CTS exchange
AP
A
B
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer
time

## Slide 43: 802.11: mobility within same subnet
H1 remains in same IP subnet: IP address can remain same
H1
BBS 2
BBS 1
switch: which AP is associated with H1?
  self-learning (Ch. 6): switch will see frame from H1 and “remember” which switch port can be used to reach H1

## Slide 44: 802.11: advanced capabilities
Rate adaptation
base station, mobile dynamically change transmission rate (physical layer modulation technique) as mobile moves, SNR (Signal-to-Noise Ratio) varies
10
20
30
40
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
operating point
1. SNR decreases, BER (Bit Error Rate) increases as node moves away from base station
2. When BER becomes too high, switch to lower transmission rate but with lower BER
= 10 log
QAM=Quadrature Amplitude Modulation
QAM2n = n bits/Hz dB = Deci-Bel
Power Out
10 Power In

## Slide 45: 802.11: advanced capabilities
power management
A node can be in one of three states:
  Transmitter on
  Receiver only on
  Dozing: Both transmitter and receivers off.
AP buffers traffic for dozing nodes.
node-to-AP: “I am going to sleep until next beacon frame”
  AP knows not to transmit frames to this node
  node wakes up before next beacon frame
beacon frame: contains list of mobile nodes with AP-to-mobile frames waiting to be sent
  node will stay awake if AP-to-mobile frames to be sent; otherwise sleep again until next beacon frame

## Slide 46: Chapter 7 outline
Introduction
Wireless
Wireless links and network characteristics
CDMA: code division multiple access
WiFi: 802.11 wireless LANs
Bluetooth

## Slide 47: Personal area networks: Bluetooth
less than 10 m diameter
replacement for cables (mouse, keyboard, headphones)
ad hoc: no infrastructure
2.4-2.5 GHz ISM radio band, up to 3 Mbps
master controller / client devices:
  master polls clients, grants requests for client transmissions
radius of
coverage
C
C
C
P
P
P
P
M
C
master controller
client device
parked device (inactive)
P
M

## Slide 48: Personal area networks: Bluetooth
Started with Ericsson's Bluetooth Project in 1994
Named after Danish king Herald Blatand (AD 940-981) who was fond of blueberries
Radio-frequency communication between cell phones over short distances
IEEE 802.15.1 approved in early 2002 is based on Bluetooth
Key Features:
  Lower Power: 10 A in standby, 50 mA while transmitting
  Cheap: $5 per device
A piconet consists of a master and several slaves. Master determines the timing and polls slaves for transmission.
Frequency hopping spread spectrum
Frequency
Time

## Slide 49: Personal area networks: Bluetooth
TDM, 625 msec sec. slot
FDM: sender uses 79 frequency channels in known, pseudo-random order slot-to-slot (spread spectrum)
  other devices/equipment not in piconet only interfere in some slots
parked mode: clients can “go to sleep” (park) and later wakeup (to preserve battery)
bootstrapping: nodes self-assemble (plug and play) into piconet
radius of
coverage
C
C
C
P
P
P
P
M
C
master controller
client device
parked device (inactive)
P
M

## Slide 50: Summary
IEEE 802.11 PHYs: 11, 11b, 11g, 11a, 11n, …
IEEE 802.11 MAC uses CSMA/CA with a 4-way handshake: RTS, CTS, data, and ack
IEEE 802.11 network consists of ESS consisting of multiple BSSs each with an AP.
802.11 Frame Format may have up to 4 addresses and includes final destination’s MAC which may not be wireless
Power management allows stations to sleep.
Bluetooth uses frequency hopping spread spectrum
Notes: IEEE 802.15.4 PHY layer allows coordinators to schedule transmissions of other nodes
ZigBee uses IEEE 802.15.4

## Slide 51
Homework 7B: WiFi Transmission
[6 points] Suppose an 802.11b station is configured always to reserve the channel with the RTS/CTS sequence. Suppose this station suddenly wants to transmit 1,200 bytes of data, and all other stations are idle at this time. Using SIFS of 13us and DIFS of 60µs, ignoring propagation delay and assuming no bit errors, calculate the time required to transmit the frame and receive the acknowledgment. Assume a frame without data (RTS/CTS/Ack) is 64 bytes long, and the transmission rate is 14 Mbps.